## Slide 1: Qualifications for the Slingers
Type of machinery and equipment | Lifting load or limited load | 
 | 1 ton and more | Less than 1 ton
Crane Mobile crane Derrick Cargo hoist | Those who have completed the slinging skill training course Those who have completed the special training course*1 Those who have approved by the Minister of Health, Labour and Welfare*2 | Those who have completed the slinging skill training course Those who have completed the special training course*1 Those who have approved by the Minister of Health, Labour and Welfare*2 Those who have completed the special education for the sling works
*1: | The training course listed in the column of training courses of Appended Table 4 of the Enforcement Ordinance on the Human Resources Development and Promotion Act
*2: | A person who has completed the training of crane operation course prescribed in the Ordinance on the Human Resources Development and Promotion Act

## Slide 2: Qualifications for the Slingers
Lifting load: 1 ton or more
Weight of load: 0.5 ton
Those who have completed the slinging skill training course
Those who have completed the special education for the sling works

## Slide 3: Definition of Cranes
Lift the loads by power
Carry the lifted loads horizontally

## Slide 4: Relationship between Magnitude and Arm of Force

## Slide 5: Moment of Leverage
Fulcrum

## Slide 6: Stationary Pulley
Pull 1 m
It will rise 1 m

## Slide 7: Tension of Sling Wire Ropes
m: Weight of the load
Fw: 9.8 x m (kN)
F1, F2: Tensions of sling wire rope
F: Resultant (kN)
F = Fw
P: Force pulling the sling wire ropes inward (kN)
Sling wire rope
Sling angle

## Slide 8: Construction of Wire Rope
Core
Wire
Strand

## Slide 9: Types of Lays
Ordinary-lay Z (right-hand)
Ordinary-lay S (left-hand)
Lang lay Z (right-hand)
Lang lay S (left-hand)
Ordinary-lay
Lang lay

## Slide 10: Measuring Method for Diameter of Wire Rope
Wrong
Correct
Diameter

## Slide 11: Number of Ropes and Sling Angle (a = Sling Angle)
Two-rope slinging with two-point
Three-rope slinging with three-point
Four-rope slinging with four-point
Diagonal

## Slide 12: Tension Factor and Sling Angle of Wire Rope
Sling angle
Tension Factor

## Slide 13: Sling Wire Rope
Eye splices at both ends
Compression joints at both ends
Endless wire rope
Wire rope with ring
Compression joint with thimble and shackle at each end
Compression joint with thimble and hook at each end

## Slide 14: Compression Jointing Method
Wire rope
Sleeve (special aluminum alloy)
Wire rope
Thimble

## Slide 15: Precautions when Using Sling Wire Rope
Sling angle
Pad
Keep in order
Single-rope slinging
Precautions for storage
Humidity
Heat
Dust
Acid
Sling angle

## Slide 16: Types of Chain
Link chain
Stud-link chain
Nominal diameter
Nominal diameter

## Slide 17: Chain Sling
Ring
Chain with ring
Chain with hook

## Slide 18: Position of Shackles

## Slide 19: Example of Using Shackles

## Slide 20: Eyebolts

## Slide 21: Eyenuts

## Slide 22: Example of Using Eyebolts
Use the washer to adjust

## Slide 23: Lifting Beam
Lifting beam

## Slide 24: Pad
Jute bag
Fabrics
Rubber sheet
Copper or copper alloy
Welded structure
Magnetic pad

## Slide 25: Bearer Blocks
Use blocks of equal size.
Hold a block from two sides with both hands.
Hold the left and right side of the block.
The load becomes unstable.
Do not put your hand on its top.

## Slide 26: Deformation of Chain
Distorted link
Bent link
Twisted link
Dent
Bend
Twist

## Slide 27: Opening and Wear of Hooks

## Slide 28: Wear of Shackles

## Slide 29: Slinging Outfits

## Slide 30: Evacuation Location
Overhead traveling crane, Bridge crane
Mobile crane, Jib crane
Evacuation location
2 m or more
longitudinal length of load
2 m or more
Traveling
Traversing
45°
Slewing
Derricking
2 m or more
Evacuation location

## Slide 31: Methods of Hanging on the Hook
Fastening wire ropes by eye

## Slide 32: Methods of Hanging on the Hook
Within 60°
Single-turn slinging

## Slide 33: Methods of Hanging on the Hook
Within 60°
One-round-turn slinging

## Slide 34: Methods of Hanging on the Hook
Within 60°
Blackwall hitch

## Slide 35: Methods of Hanging on the Hook
Effective rope
Guide rope
Looping
Looping

## Slide 36: Methods of Securing Wire Ropes to Load
When sling wire ropes are loosened, eyes may be removed.
Fastening wire ropes by eye

## Slide 37: Methods of Securing Wire Ropes to Load
Sling angle
Sling angle
Two-rope slinging with four-point
Two-rope slinging with four-point
Single-turn slinging

## Slide 38: Methods of Securing Wire Ropes to Load
Two-rope slinging with two-point (noosing with shackles)

## Slide 39: Methods of Securing Wire Ropes to Load
Noosing to same direction
Noosing to different directions
Two-rope slinging with two-point (fastening by eyes)

## Slide 40: Methods of Securing Wire Ropes to Load
The bolt rotates.
The bolt does not rotate.
How to use shackles (Take attention for bolt position)

## Slide 41: Methods of Securing Wire Ropes to Load
Fastening wire ropes by eye (Take attention for compression joint position)

## Slide 42: Methods of Securing Wire Ropes to Load
One-round-turn slinging with two-rope and four-point

## Slide 43: Methods of Securing Wire Ropes to Load
One-round-turn noosing with two-rope and two-point

## Slide 44: Methods of Securing Wire Ropes to Load
Single-turn slinging
Fastening wire ropes by eye
Passing doubled over part through eye
Passing eyes through a sling wire rope doubled over
Use endless wire rope
Bale sling hitch

## Slide 45: Methods of Securing Wire Ropes to Load
Sling angle
Slinging with single hitch on bottom

## Slide 46: Methods of Securing Wire Ropes to Load
Single-rope slinging

## Slide 47: Chain with Clamp

## Slide 48: Chain with Sling Hook

## Slide 49: Endless Chain for Hacker

## Slide 50: Chain with Fundry Hook (with Wide Opening)