## Slide 1: Gas Welding (Gasu Yousetsu) Skill Training Supplementary Text PowerPoint Training Materials

## Slide 2: Chapter 1 Equipment Used for Gas Welding (Gasu Yousetsu), etc.

## Slide 3: Gas welding (Gasu Yousetu) characteristics
Advantages
・ You can work anywhere with a gas cylinder (bonbe).
・ Welding can be done without using a covered electrode.
・ Less fumes (hyumu) and spatter (supatta) generated.
Text Page 2/Supplementary Text Page 6
Gas cutting (gasu setudan) characteristics
Advantages
・ Can cut even thick plates.
Disadvantages
・ The temperature of the heat source is low.
・ It takes a long time to heat the metal until it melts.
・ It is difficult to overheat the welded part locally.
・ A lot of strain is generated.
・ The heat-affected zone is large.
・ Not suitable for welding different metals or thick plates.
Disadvantages
・ Only iron-based materials, etc., can be cut.

## Slide 4: Equipment used for gas welding (gasu yousetu)/gas cutting (gasu setudan))
Text Page 6/Supplementary Text Page 9
Fall prevention chain
Fuel gas
Oxygen (sanso)
Source: Partially revised figures from the National Institute of Occupational Safety and Health Technical Guidelines
Fig. 1-1 Equipment used for gas welding (gasu yousetsu) and gas cutting (gasu setudan))
(1) Oxygen (sanso) pressure regulators (aturyoku chousei ki))
(2) Fuel gas pressure regulator (aturyoku chousei ki)
(3) Oxygen (sanso) hose (housu) (blue)
(4) Fuel gas hose (housu) (red or orange)
(5) Welder or cutter (setudanki) (suction pipe and nozzle (higuchi))
(*Figure shows an example of a cutter (setudanki))
(6) Flashback arrester (kanshiki anzen ki) for oxygen (sanso) (flashback (gyakka) prevention device)
(7) Flashback arrester (kanshiki anzen ki) for fuel gas (flashback (gyakka) prevention device)

## Slide 5: Torch (tochi) (welder and cutter (setudanki))
Text Pages 9, 10/Supplementary Text Page 11
Fig. 1-4 Type-B welder (French style)
Source: KOIKE SANSO KOGYO Co.,LTD.
Torch (tochi) head
Nozzle (higuchi)
Mixing tube nut
Mixed gas tube
Oxygen (sanso) valve
Fuel gas valve
Fuel gas inlet
Fig. 1-5 Low-pressure (torch (tochi) mixing) cutter (setudanki) (French style)
Source: KOIKE SANSO KOGYO Co.,LTD.
Torch (tochi) head
Nozzle (higuchi)
Mixing tube
Cutting oxygen (setudan sanso) tube
Mixer
Preheated oxygen (sanso) valve
Cutting oxygen (setudan sanso) valve
Fuel gas valve
（小池酸素工業株式会社提供）
（小池酸素工業株式会社提供）

## Slide 6: Nozzle (higuchi)
Flammable gas types and nozzles (higuchi)
The structure of the nozzle (higuchi) is different for each flammable gas
Text Page 14/Supplementary Text Page 12
Dangers of using incorrect flammable gas types
If acetylene (asechiren) gas is used with a nozzle (higuchi) for other flammable gases, a flashback (gyakka) will occur, which is extremely dangerous
Table 1-3 Acetylene (asechiren) gas and propane (puropan) gas combustion rates
Acetylene (asechiren)
Propane (puropan)
Minimum ignition temperature
(In oxygen (sanso))
Combustion rate
(Neutral mixture ratio)
*: The figures are based on “Summary: Thermal Cutting Q&A” from The Japan Welding Engineering Society.

## Slide 7: Pressure regulator (aturyoku chousei ki)
Acetylene (asechiren) pressure regulators (aturyoku chousei ki))
Text Pages 19, 20/Supplementary Text Pages 14, 15
Oxygen (sanso) pressure regulators (aturyoku chousei ki))
Fig. 1-17: Acetylene (asechiren) gas regulator
Source: NISSAN TANAKA CORPORATION
Fig. 1-18: Oxygen (sanso) regulator mounting screws
Mounting nut type (German style)
Mounting screw type (French style)
Source: KOIKE SANSO KOGYO Co.,LTD.
（小池酸素工業株式会社提供）
（日酸TANAKA(株)提供）

## Slide 8: Welding hose (housu)
Display for rubber hose for welding/cutting (yousetu/setudan you gomu housu)
・ Manufacturer or supplier mark
・ Hose (housu) type number
・ Maximum working pressure
・ Nominal diameter (inner diameter)
・ Gas type (Table 1-5)
・ Year of manufacture
Text Page 24, 25/Supplementary Text Page 17
[Display example]
This symbol provides the following information.
(1) The manufacturer is “XYZ.”
(2) The hose (housu) type is “Type 1.”
(3) The maximum working pressure is 2MPa.
(4) The nominal diameter is 10 mm.
(5) The gas type is oxygen (sanso).
(6) The year of manufacture is 2019.
Table 1-5: Gas type symbols and identifying colors (JIS K 6333)
Gas type symbol
Gas type
Color of exterior rubber layer
Gas for acetylene (asechiren) and other fuels (*)
(Excluding LPG, MPS, natural gas, and methane)
Air, nitrogen, argon, carbon dioxide
Oxygen (sanso)
LPG, MPS, natural gas, methane
Acetylene (asechiren), LPG, MPS, natural gas, methane, and other fuel gases
*Manufacturers must consider suitability for hydrogen applications
Red
Blue
Black
Orange
Red and orange

## Slide 9: Various gas containers (cylinder (bonbe)) and acetylene (asechiren) gas generators (1) Gas container displays and colors
Filling labels for gas containers
・ Filling gas name
・ Filling pressure or mass at the time of filling
・ Filling date/manufacturing lot identifier
・ Store (seller) contact information/factory (manufacturer) contact information
・ Filling gas properties
・ General notes
・ Contains explanations of priority items,
etc.
Text Pages 27, 28/Supplementary Text Page 18
Filling gas
Table 1-9: Gas container colors
Container color
Oxygen (sanso)
Acetylene (asechiren)
Hydrogen
Liquefied ammonia
Liquefied carbon dioxide gas
Liquefied chlorine
Other gases
(LPG, etc.)
Black
Brown
Red
White
Green
Yellow
Gray

## Slide 10: Various gas containers (cylinder (bonbe)) and acetylene (asechiren) gas generators (2) Acetylene gas cylinders
Text Page 28/Supplementary Text Page 19
Container valve
Cap
Soluble alloy plug
Container body
Mass
Ventilation hole
O-ring
Ground nut
Spindle
Soluble alloy plug safety valve
Gas outlet
Packing
Filter
Source: National Institute of Occupational Safety and Health Technical Guidelines
Fig. 1-25: Acetylene (asechiren) container and container valve
Ground packing

## Slide 11: Various gas containers (cylinders (bonbe)) and acetylene (asechiren) gas generators (3) Other cylinders
Other flammable gas cylinders (bonbe))
For propane (puropan) and butane, etc., fill the cylinder (bonbe) in a high-pressure liquid state
The caps for flammable gas (and helium) cylinders (bonbe) have left-hand threads
Text Page 30/Supplementary Text Page 20
Oxygen cylinder (sanso bonbe)
Oxygen (sanso) fills the cylinder (bonbe) in a gaseous state
The caps (filling mouth) of oxygen cylinders (sanso bonbe) have right-hand threads, the opposite of flammable gas
Oxygen (sanso) helps things burn and is extremely dangerous.

## Slide 12: Various gas containers (cylinders (bonbe)) and acetylene (asechiren) gas generators (4) Gas manifold
Text Pages 31/Supplementary Text Page 21
Pressure regulator (aturyoku chousei ki)
Source: National Institute of Occupational Safety and Health Technical Guidelines
Safety valve
To the factory
Piping
Connecting pipe
Fig. 1-28: Conceptual diagram of oxygen (sanso) gas manifold

## Slide 13: Cylinder (bonbe) and acetylene (asechiren) generator (1) Notes for transporting and using cylinders
Text Pages 34, 36, 37/Supplementary Text Pages 23, 24
Notes for transporting cylinders (bonbe)
During vehicle transportation, must be upright or tilted, and must be directly secured to a dedicated tool or vehicle
Use dedicated cylinder (bonbe) carriers for transportation at factories and construction sites
When carrying cylinders (bonbe) by hand, the valve part of the container must not be held
Notes for using cylinders (bonbe)
  Be sure to secure the cylinder (bonbe)
  Do not use cylinders (bonbe) on the loading platform of a transport vehicle
  When securing the cylinder (bonbe), do not secure it at the neck
  Do not touch the oxygen cylinder (sanso bonbe) with oily gloves. Also, do not place oil near the cylinder (bonbe).

## Slide 14: Cylinder (bonbe) and acetylene (asechiren) generator (2) Notes for cylinder disposal and return
Text Page 37/Supplementary Text Page 25
・ Do not leave cylinders (bonbe) in the factory as-is or dispose of them as general industrial waste.
・ Never cut a container filled with oxygen (sanso) or flammable gas.
・ The gas container must be returned to the manufacturer without all of the gas being used up.

## Slide 15: Pressure regulator (aturyoku chousei ki) (1) Fitting procedure
Text Page 41/Supplementary Text Page 26
[Pressure regulator (aturyoku chousei ki) fitting procedure]
(1) Remove dust, etc.
(2) Check the packing
(3) Install the pressure gauge
(4) Check the control handle
(5) Open the valve
(6) Check for gas leaks

## Slide 16: Pressure regulators (aturyoku chousei ki) (2) Notes for use
Text Page 43/Supplementary Text Page 27
[Notes for using pressure regulators (aturyoku chousei ki)]
(1) When not in use, turn the control handle all the way to the left to loosen it.
(2) Do not apply grease or oil to the regulator parts or handle them with oily gloves. In particular, do not get any oil on the oxygen (sanso) pressure regulator (aturyoku chousei ki).
(3) If the mounting screw of the pressure regulator (aturyoku chousei ki) is damaged, do not try to forcibly install it.
(4) Do not move a cylinder (bonbe) with a pressure regulator (aturyoku chousei ki) installed to it.
(5) If the acetylene (asechiren) pressure drops during work, check the amount remaining inside the cylinder (bonbe).
(6) When work is finished or being suspended, close the cylinder (bonbe) valve and turn the control handle all the way to the left to loosen it.
(7) Do not disassemble or repair the pressure regulator (aturyoku chousei ki).

## Slide 17: Welders, etc. (1) Fitting
Text Page 43/Supplementary Text Page 28
[Pressure regulator (aturyoku chousei ki) and welder connection procedures]
(1) Before connecting, check that the hose (housu) has not deteriorated or have cracks.
(2) Make sure that there are no dust, insects, or water inside the hose (housu).
(3) Make sure that the blowpipe (suikan) valve is closed.
(4) Use a blue hose (housu) for oxygen (sanso) and a red hose for acetylene (asechiren). Do not share hoses (housu) for different types of gas.
(5) If one-touch type connectors are attached to both ends of the hose (housu), securely connect the output side of the pressure regulator (aturyoku chousei ki) to the blowpipe (suikan). At this time, if the flammable gas pressure regulator (aturyoku chousei ki) does not have a flashback arrester (kanshiki anzen ki), install a flashback arrester on the hose (housu) side of the flammable gas.
(6) After all the connections are completed, set the oxygen (sanso) pressure to about 0.3 to 0.5 MPa and check for gas leaks using soapy water or the like. After checking for oxygen (sanso) gas leaks, set the pressure of the flammable gas to about 0.03 to 0.05 MPa and perform a gas leak check in the same manner.
(7) If there is no gas leak, open the valve of the flammable gas in the blowpipe (suikan) for 2 to 3 seconds to release the gas, and repeat this twice. Next, with the flammable gas valve closed, open the oxygen (sanso) gas valve for about 5 seconds to release the oxygen.
(8) Finally, close the blowpipe (suikan) valve, close the cylinder (bonbe) valve, loosen the pressure regulator (aturyoku chousei ki) completely, and wait for about 5 minutes. After that, check the pressure on the high-pressure side and low-pressure side of the pressure regulator (aturyoku chousei ki).

## Slide 18: Welders, etc. (2) Adjusting the low-pressure side pressure for a pressure regulator (aturyoku chousei ki)
Text Page 44/Supplementary Text Page 29
[Procedure for adjusting the low-pressure side pressure for a pressure regulator (aturyoku chousei ki)]
(1) Re-confirm that the blowpipe (suikan) valve is closed.
(2) Slowly turn the control handle for the oxygen (sanso) and flammable gas with the pressure regulator (aturyoku chousei ki) to adjust the pressure on the low-pressure side.
The appropriate pressure differs depending on the nozzle (higuchi) and is described in the manual, etc., of the nozzle manufacturer. Generally, oxygen (sanso) is 0.2 to 0.3 MPa, and flammable gas is 0.02 to 0.03 MPa.

## Slide 19: Welders, etc. (3) Ignition and flame control
Text Page 44, 45/Supplementary Text Page 30
[Ignition and flame control procedure]
(1) Wear protective welding gear and light-shielding protective glasses for gas welding (gasu yousetu) in an appropriate manner.
(2) Open the blowpipe (suikan) flammable gas valve.
(3) Ignite using special ignition equipment (welding lighter (yousetu you raita)).
(4) Open the preheated oxygen (sanso) valve as soon as possible. Operate the flammable gas valve first, followed by the oxygen (sanso) valve, to create a pale flame. At this time, the white conical section (white cone (white spots)) formed at the mouth of the nozzle (higuchi) in the gas flame should emerge from the tip of the nozzle by about as much as is shown in Fig. (2) of Fig. 1-30. The flame that is in an appropriate state at this time is called a neutral flame or standard flame.
Fig. 1-30: Adjusting the flame
(1) Flame immediately after ignition (carbonizing flame)
(2) After adjusting the amount of oxygen (sanso) (standard flame)
Source: KOIKE SANSO KOGYO Co.,LTD.
（小池酸素工業株式会社提供）

## Slide 20: Welders, etc. (3) Welding
Text Page 45/Supplementary Text Page 31
[Gas welding (gasu yousetu) procedure]
(1) Set the base material to be welded in the joint.
(2) Heat one end of the base material joint so that the distance between the surface of the base material and the tip of the white cone is about 2 to 3 mm. After a while, the surface of the base material that is exposed to the flame will turn red, and a welding pool will form in the center. The welding pool should look shiny. If both base materials do not fuse, fuse them by adding a covered electrode.
(3) When one end of the base material joint is fused, weld the other end of the joint in the same manner. This is called tack welding and will temporarily fix the joint of the base material. When welding thin plates, the number of tack welds can be reduced to prevent the strain from growing large.
(4) Next, form a welding pool at one end of the base material joint and perform welding while moving the torch (tochi) toward the joint so as to keep it at a constant size. When welding thin plates, do not add more covered electrodes than necessary. On the contrary, when the plate thickness of the base material is large, melt the base material at a position close to the white cone and weld it while adding a covered electrode.

## Slide 21: Welders, etc. (4) Cutting
Text Page 46/Supplementary Text Page 32
[Gas cutting (gasu setudan) procedure]
(1) Set the base material to be cut.
(2) Begin by using a preheating flame (yonetu en) to apply a white cone to the spot to be cut to make the base material glow red.
(3) While keeping the blowpipe (suikan) slightly tilted, slowly move it along the line you want to cut. At this time, take care to keep the distance between the nozzle (higuchi) and the base material constant, and move it at a constant speed so that the cutting spatter flies directly below.

## Slide 22: Welders, etc. (5) Notes for welding/cutting work
Text Page 46/Supplementary Text Page 33
[Notes for welding/cutting work]
・ If you hear an occasional clicking sound after ignition, the nozzle (higuchi) may be loose or scratched. Extinguish the fire immediately, tighten the nozzle (higuchi), and replace the nozzle if the problem persists.
・ If there is a crackling noise from the blowpipe (suikan) during welding or cutting work, there may be a flashback (gyakka). Immediately stop work, clean and retighten the nozzle (higuchi), check for gas leaks, etc.
・ The following are possible causes of flashback (gyakka).
[Causes of flashback (gyakka)]
The mixing ratio of oxygen (sanso) and flammable gas changed.
Foreign matter such as spatter (supatta) entered the nozzle (higuchi).
The tip of the nozzle (higuchi) was blocked due to hitting the base material, etc.
The temperature of the nozzle (higuchi) rose.
The nozzle (higuchi) was not sufficiently tightened.
Air entered the flammable gas supply system.

## Slide 23: Welders, etc. (6) Fire extinguishing method
Text Page 47/Supplementary Text Page 34
[Fire extinguishing method]
When extinguishing a fire, first close the preheated oxygen valve, then close the fuel gas.
For cutting work, close the valves in the following order: cutting oxygen (setudan sanso), preheated oxygen, and fuel gas.
If the fire goes out during welding/cutting work, close the valves immediately in the same order.
However, if a flashback (gyakka) occurs during work, immediately close the preheated oxygen valve, then close the fuel gas valve, and finally close the cutting oxygen (setudan sanso) valve. Next, close the oxygen (sanso)/fuel gas container valve and loosen the pressure control handle (aturyoku chousei handoru).
If the fire is extinguished due to a flashback (gyakka), identify the cause and take countermeasures before resuming work. Do not restart without identifying the cause.

## Slide 24: Nozzle (higuchi)
Text Page 47/Supplementary Text Page 35
[Nozzle (higuchi) fitting procedure]
(1) Make sure that the contact parts between the nozzle (higuchi) and the blowpipe (suikan) are not scratched and that there are no contaminants or oil on them.
(2) Completely return the back nut (packing nut) in Fig. 1-31 (until it hits the hexagonal part of the main body).
(3) Screw the nozzle (higuchi) into the blowpipe (suikan) as far as it will go.
(4) Fully tighten the hexagonal part of the nozzle (higuchi) body with a dedicated wrench. If a monkey wrench is used at this time, the outer tube nut may rotate, so a monkey wrench should not be used.
(5) Rotate the back nut by hand until you feel resistance.
(6) Rotate the back nut with a dedicated wrench. When installing it for the first time, it should be at 1/2 rotation. The second and subsequent fittings should be at about 1/4 rotation.
[Nozzle (higuchi) selection]
The nozzle (higuchi) must be selected appropriately according to the type of flammable gas used and the thickness of the base material.
Fig. 1-31: Nozzle (higuchi) fixing
Source: KOIKE SANSO KOGYO Co.,LTD.
Back nut
Hexagonal part of the main body
Dedicated wrench
（小池酸素工業株式会社提供）

## Slide 25: Hose (housu) (1) One-touch joint (wantacchi tugite) fitting
Text Page 50/Supplementary Text Page 36
[One-touch joint (wantacchi tugite) fitting procedure for both ends of hose (housu) ]
(1) Firmly secure it with a hose band (housu bando). At this time, do not use oil or grease, forcibly twist it, scrape the inner surface, or tap to soften it.
(2) Plug the hose (housu) joint tightly, immerse it in a water tank, apply a pressure of about twice the maximum working pressure for 5 minutes with nitrogen or dry air (only for objects without any oiliness), and verify that there is no leakage or disconnection of the joint.
Source: NISSAN TANAKA CORPORATION
Fig. 1-36: Example of gas welded one-touch joint (wantacchi tugite)
（日酸TANAKA(株)提供）

## Slide 26: Hose (housu) (2) Gas hose visual inspection
Text Page 51/Supplementary Text Page 37
[Gas hose (housu) pre-use visual inspection items]
  Cracks that extend to the reinforcing layer on the hose (housu) surface
  Wear or swelling
  Discoloration /hardening
  Metal joint chafing
  Inspect the oxygen (sanso) hose (housu) interior for foreign matter (contaminants, insects, etc.)
  *In particular, if the oxygen (sanso) hose (housu) has a flashback (gyakka) even once, soot will adhere to the interior, and if there is another flashback, it may violently combust, so be careful.
  *If even one spot is abnormal, do not repair, but replace with a new hose (housu). Do not repair leaking parts of a hose with insulating tape, etc..

## Slide 27: Hose (housu) (2) Precautions when handling gas hoses
Text Page 52/Supplementary Text Page 37
[Notes for using gas hoses (housu)]
  Do not use below the minimum bending radius
  Do not use by slinging over the neck of the cylinder (bonbe) or the shoulders of the operator
  Do not apply oils or fats to the hose (housu)
  Do not repair and use scratched items
  Do not hang it on a nail when storing
  Do not store in a place where ozone is generated

## Slide 28: Inspection of equipment used for gas welding (gasu yousetu) (1) The necessity of inspections
Text Page 53/Supplementary Text Page 38
Table 1-17: Timing of disposal of equipment used for various welding operations or inspections by the manufacturer
Target device
First inspection
Second and subsequent inspections
Start time
Period
Period
Period specified by the manufacturer
Pressure regulator (aturyoku chousei ki)
Period specified by the manufacturer
Suction tube
Flashback arrester (kanshiki anzen ki)
Period specified by the manufacturer
After manufacture date
After starting to use
After manufacture date
5 years
3 years
7 years
Source: National Institute of Occupational Safety and Health Technical Guidelines

## Slide 29: Inspection of equipment used for gas welding (gasu yousetu) (2) Blowpipe (suikan) (torch (tochi)) inspection
Text Page 53/Supplementary Text Page 39
Table 1-18: Inspection items (example)
Inspection item
Visual inspection
Airtightness inspection
Check the flame state
Body, hose (housu), joint stand, and pipe
Locations to inspect
Details of inspection
Daily inspection (nichijou tenken)
Periodic monthly inspection
Valve, etc.
Nozzle (higuchi)
Nozzle (higuchi) contact, hose (housu) joint base contact
Fitting sections for valves and parts
Nozzle (higuchi) fitting section
Valve
Flame
Cutting oxygen (setudan sanso) airflow
Are there any cracks or corrosion?
Is there any damage or
deformation?
Is there any deformation or melting damage?
Are there any scratches or deformation?
Is there any external leakage?
Are there any gas leaks?
Is there a sheet leak?
Can it be adjusted smoothly?
Is it normal?

## Slide 30: Inspection of equipment used for gas welding (gasu yousetu) (3) Pressure regulator (aturyoku chousei ki) inspection
Text Page 54, 55/Supplementary Text Page 40
Fig. 1-40: Names of pressure regulator (aturyoku chousei ki) parts
Low-pressure side pressure gauge
High-pressure side pressure gauge
Outlet joint
Inlet joint
Set screw
Nut
Table 1-19: Inspection items (example)
Inspection item
Visual inspection
Airtightness inspection
Verification of specification pressure range
Body, cover
Locations to inspect
Details of inspection
Daily inspection (nichijou tenken)
Periodic monthly inspection
Junctions and screws between the inlet joint and the container valve
(1) Inlet joint screw-in section
(2) High-pressure pressure gauge screw-in section
(3) Back cap screw-in section
Pressure gauge case
Is it possible to supply gas and operate the pressure control handle (aturyoku chousei handoru) to set the maximum pressure normally?
(4) Body and cover screw-in section
(5) Low-pressure pressure gauge screw-in section
(6) Outlet joint screw-in sections
(7) Safety valve
Outlet
Are there any cracks or corrosion?
Is there any damage or deformation?
Supply gas with the pressure control handle (aturyoku chousei handoru) while it is loose and check for gas leaks with soapy water
Are there any scratches, deformation, or weak adhesiveness?
Are there any gas leaks (outflow)?
Set the working pressure with the outlet closed and check for gas leaks with soapy water.
Verification of pressure drop
Inlet joint, outlet joint, pressure gauge
Pointer position
Are there any gas leaks from the safety valve outlet?
Does the high-pressure pressure gauge decrease when gas is allowed to flow during use?
Is there any deformation?
Does it return to the zero position?

## Slide 31: Chapter 2 Basic Knowledge about Flammable Gases and Oxygen (sanso)

## Slide 32: Oxygen (sanso) risks
Text Page 57/Supplementary Text Page 42
・ High concentrations of oxygen (sanso) are extremely dangerous and also harmful to the human body.
・ Low concentrations have serious adverse effects on human health.
・ The combustion temperature in oxygen (sanso) is higher than when combusting in air.
Table 2-1: Ignition temperature of substances (℃)
In the air
In oxygen (sanso)
Gasoline
Kerosene
Heavy oil
Sawdust
Hydrogen
Source: Kogaku Komamiya, “Dangers of Oxygen and Disaster Prevention Measures” (from the Research Institute of Industrial Safety, 1961)

## Slide 33: Flammable gases (1) The 3 elements of combustion
Text Page 60/Supplementary Text Page 44
[The 3 elements of combustion]
・ A flammable object
・ Oxygen (sanso)
・ An ignition source
If one of these three elements of combustion is missing, in principle, no explosion occurs.

## Slide 34: Flammable gases (2) Lower explosive limit (bakuhatu kagen kai) and upper explosive limit
Text Page 60/Supplementary Text Page 44
[Lower explosive limit (bakuhatu kagen kai) and upper explosive limit]
If flammable gas leaks into the air, it will not explode unless it is within a certain concentration range. This range is called the combustion (explosion) range. A gas with a small lower explosive limit enters the explosion range when just a small amount of it leaks.

## Slide 35: Overview of flammable gases (3) Combustion rate
Text Page 62/Supplementary Text Page 45
Fig. 2-1: Formation of flame surface (white cone)
Gas combustion rate
Gas combustion rate
Gas combustion rate
Gas combustion rate
White cone (white spots)
Gas ejection speed
White cone (white spots)
Dead band
Gas ejection speed
Gas ejection speed
Gas ejection speed
[Standard]
Blowout
Flashback (gyakka)
Source: KOIKE SANSO KOGYO Co.,LTD.
（小池酸素工業株式会社提供）

## Slide 36: Overview of flammable gas (4) Minimum ignition energy and ignition source
Text Page 63/Supplementary Text Page 46
[Minimum ignition energy]
When the concentration of flammable gas reaches the explosive limit value, the gas explodes if there is a certain amount of energy.
[Ignition source]
Depending on the condition of the flammable gas, gas explosions can occur even due to the electrostatic energy from the human body.
In addition, there are many ignition sources in the workplace, such as electric motors, pilot fires for gas appliances, high-temperature objects, frictional heat, and impact sparks.
In order to prevent explosions during welding work, it is necessary to prevent leakage of flammable gas.

## Slide 37: Flammable gases used for welding, etc. (1) Physical properties, etc.
Text Page 65/Supplementary Text Page 47
Table 2-6: Physical properties, etc., of gases used for welding, etc.
Color and odor
Chemical formula
Minimum ignition temperature
Gas specific gravity (Note 2)
Boiling point
Other
Acetylene (asechiren)
A colorless, odorless gas. Acetylene (asechiren) used for welding features a distinct odor belonging the solvent and impurities used for dissolving and for filling the container.
(Note 1)
A colorless, odorless gas. Propane (puropan) used in ordinary households is required by the High Pressure Gas Safety Act to have an odorant, but this is not required for industrial LPG.
A colorless, odorless gas.
Propane (puropan)
Hydrogen
The flame temperature is high compared to other flammable gases for welding, making it suitable for gas welding (gasu yousetu).
Note 1: This odor is quite different from the odor of household propane (puropan) gas.
2: Weight ratio compared to air. If it is smaller than 1, it may accumulate near the ceiling, and if it is larger than 1, it may accumulate in the pit, etc.

## Slide 38
Text Page 66/Supplementary Text Page 48
[Risks]
Acetylene (asechiren) gas, propane (puropan) gas and hydrogen are highly flammable and ignitable gases, and they may explode if the gas container heats up. Hydrogen easily ignites, and the flame is hard to see.
[Risk of harm]
Acetylene (asechiren) gas, propane (puropan) gas, and hydrogen are extremely dangerous because they may cause oxygen deficiency (sanso ketubou) when inhaled at high concentrations. It is also said that inhaling acetylene (asechiren) gas may cause pulmonary edemas. In addition, inhaling acetylene (asechiren) gas or propane (puropan) gas may cause drowsiness or dizziness, hypoesthesia, and headache.
[Notes for fire outbreaks]
Use dry chemicals (hunmatu shouka zai) or inert gases (N2, Ar, CO2, etc.) to extinguish fires caused by acetylene (asechiren) gas, propane (puropan) gas, and hydrogen. If there’s a big fire, sprinkle or spray water onto it. Straight steaming should not be performed.
Flammable gases used for welding, etc. (2) Risks

## Slide 39: High-pressure gas (1) Types of high-pressure gas
Text Page 67/Supplementary Text Page 49
[Types of high-pressure gas] (From the High Pressure Gas Safety Act)
(1) Compressed gas
Compressed gas refers to compressed gas whose pressure (meaning gauge pressure; the same applies hereafter) is 1 MPa or higher at normal temperatures and with a pressure that is actually 1 MPa or higher, or 1 MPa or higher at a temperature of 35°C (excluding compressed acetylene (asechiren) gas)
(2) Compressed acetylene gas
Compressed acetylene (asechiren) gas whose pressure is 0.2 MPa or higher at normal temperatures and with a pressure that is actually 0.2 MPa or higher, or 0.2 MPa or higher at a temperature of 15°C.
(3) Liquefied gas (ekika gasu)
(D) Liquefied gas (ekika gasu) refers to liquefied gas whose pressure is 0.2 MPa or more at normal temperature and whose pressure is actually 0.2 MPa or more or attains pressure of 0.2 MPa at a temperature of 35°C or less

## Slide 40: High-pressure gas (2) Risks associated with high-pressure gas
Text Pages 67, 69/Supplementary Text Page 50
[Risks of being compressed]
(1) Occurrence of ruptures
(2) Cylinder (bonbe) flight accidents
[Notes for handling high-pressure gas]
High-pressure gas storage method: Must be stored in locations below 40°C
Table 2-8: Changes in pressure due to temperature
Tempe-rature (℃)
Gas pressure in the container (MPa)
Value when the pressure at 25°C is 1

## Slide 41: Disasters that occur due to gas welding (gasu yousetu)
Text Page 74/Supplementary Text Page 51
[Health disorders caused by fumes (hyumu)]
Although not as many fumes (hyumu) are generated by gas welding (gasu yousetu) as by arc welding, there are concerns about the occurrence of pulmonary edemas due to the welding and cutting of galvanized base materials, and lung cancer and asthma due to the cutting of stainless steel.
Additionally, in recent years, the health effects of welding and cutting of copper materials containing manganese on the central nervous system have become an issue.

## Slide 42: Preventing disasters due to gas welding (gasu yousetu) (1) Preventing burns
Text Page 75/Supplementary Text Page 52
The Ordinance on Industrial Safety and Health requires workers to wear protective goggles and protective gloves for welding work, etc., done with acetylene (asechiren) welding equipment and gas welding (gasu yousetu) equipment using manifolds.
Figu. 2-10: Welding protective equipment
Source: Caterpillar Operator Training Ltd.
Safety shoes
Foot cover
Apron
Face shield for welding
Arm cover
Hard hat
Protective goggles
Dustproof mask
Protective gloves made of leather for welding
（キャタピラー教習所株式会社提供）

## Slide 43: Preventing disasters due to gas welding (gasu yousetu) (2) Conditions surrounding explosions and fires
Text Pages 75, 77/Supplementary Text Page 53
[Conditions and causes surrounding explosions and fires]
In most cases of explosions and fires during gas welding (gasu yousetu) work, flammable gas for welding exploded or erupted in flames. The causes include leakage due to improper fitting of equipment and hoses (housu) and leakage from deteriorating facilities, as well as flashbacks (gyakka).
[Dust explosion (hunjin bakuhatu)]
If gas welding (gasu yousetu) is performed in locations where flammable material (kanensei no mono) become fine particles (dust) and float through the air in large quantities, a violent explosion could occur.
It should be noted that dust can occur not only from flour, sugar, and plastic, but also in metals such as aluminum and iron that do not burn in bulk as long as they are flammable, even if they are not a substance such as coal.

## Slide 44: Preventing disasters due to gas welding (gasu yousetu) (3) Preventing explosions and fires
Text Pages 77, 79, 81/Supplementary Text Pages 55, 55, 56
[Preventing explosions caused by fuel gas]
・ In order to prevent explosions, it is essential to eliminate the leakage of fuel gas
・ Secure sufficient ventilation of the workplace on a daily basis
[Preventing disasters due to flashbacks (gyakka)]
・ Make sure to purge the gas before starting work
・ Reliable inspection and maintenance of equipment
・ Handling flammable gases and oxygen (sanso) in accordance with standards
・ Secure fitting of safety units (anzen ki)
[Preventing fires due to causes other than fuel gas]
・ Eliminate flammable materials (kanensei no mono), etc.
・ Take care during mixed work or proximity work (including vertical work), etc.

## Slide 45: Preventing disasters due to gas welding (gasu yousetu) (4) Harmful rays (yuugai kousen) and oxygen deficiency (sanso ketubou)
Text Pages 82, 86/Supplementary Text Page 57
[Harmful rays generated during gas welding (gasu yousetu)]
During gas welding (gasu yousetu) work, strong infrared rays are generated by high-temperature parts such as base materials and flames.
Occupational diseases caused by infrared rays: eye disorders such as retinal burns and cataracts, skin diseases
[Oxygen deficiency (sanso ketubou)]
When gas welding (gasu yousetu) or fusing is performed in locations with insufficient ventilation, in addition to performing forced ventilation with portable ventilation devices, use appropriate respiratory protective devices (kokyuu you hogo gu) according to the situation.
Oxygen deficiency (sanso ketubou): a condition in which the concentration of oxygen in the air is less than 18%

## Slide 46: Preventing disasters due to gas welding (gasu yousetu) (5) Disasters caused by metal fumes (hyumu)
Text Pages 86, 88/Supplementary Text Pages 58, 59
[Pneumoconiosis (jinpai) and complications]
Pneumoconiosis (jinpai) and its complications represent the most serious chronic disorder caused by metal fumes (hyumu).
Complications especially related to pneumoconiosis (jinpai)
● Pulmonary tuberculosis ● Tuberculous pleurisy ● Secondary bronchitis
● Secondary bronchiectasis ● Secondary pneumothorax ● Primary lung cancer
[Generation of metal fumes (hyumu)]
Fumes (hyumu) are high-temperature metals that turn into steam and are released into the work environment, cooled in the air, and solidify. In gas welding (gasu yousetu) and gas cutting (gasu setudan), in addition to the base materials, the metal contained in the surface plating also turns into fumes (hyumu).
[Countermeasures for metal fumes (hyumu)]
・ Adoption of low-fume (hyumu) molten material
・ Engineering measures
・ Administrative measures
・ Individual protective devices

## Slide 47: Preventing disasters due to gas welding (gasu yousetu) (6) Heatstroke (necchuushou) and fall accidents (tuiraku saigai)
Text Pages 92, 93/Supplementary Text Page 60
[Heatstroke (necchuushou) prevention measures
Managing one’s daily physical condition is also important for heatstroke (necchuushou), so do not work constantly and be sure to take appropriate breaks. Especially when in narrow locations or outdoors during summer, work is performed in places with high temperatures, high humidity, and harsh sunlight. Under such conditions, it is important to pay attention to the WBGT (heat index) and to supply oneself with enough water and salt when working. Japanese tea and other beverages that contain caffeine are diuretics, and they are not suitable as a countermeasure for heatstroke (necchuushou).
[Preventing fall accidents (tuiraku saigai)]
When welding at high altitudes, make sure to use fall prevention equipment (tuiraku seishi you kigu) properly to prevent fall accidents (tuiraku saigai). (Special training for full harnesses is required)

## Slide 48: Chapter 3 Applicable Laws and Regulations

## Slide 49: Legal system related to gas welding (gasu yousetu), etc.
Text Page 101/Supplementary Text Page 61
Industrial Safety and Health Act (roudou anzen eiseihou)
Pneumoconiosis (jinpai)
Working Environment Measurement Law (*)
Industrial Safety and Health Act Enforcement Ordinance
Enforcement Ordinance of the Working Environment Measurement Law
Industrial Safety Rules
Lead poisoning prevention rules
Ordinance on Prevention of Hazards Due to Specified Chemical Substances
Ordinance on Prevention of Anoxia, etc.
Ordinance on Prevention of Hazards Due to Dust (*Applicable when performing metal gas cutting (gasu setudan) in indoor workplaces, etc.)
Ordinance on Examination of Machines and Other Equipment
Standards for safety units (anzen ki) for acetylene (asechiren) welding equipment and safety units for gas welding (gasu yousetu) equipment using manifolds
Acetylene (asechiren) generator structural standards for acetylene welding equipment
Enforcement Ordinance of Pneumoconiosis (jinpai) Law
Enforcement Regulations of the Working Environment Measurement Law
*Work environment measurements are performed when the base material contains a substance such as manganese.