## Slide 1: Vehicle-type Construction Machinery Operation (Leveling, Transportation, Loading and Excavation) Skill Training Auxiliary Text Power Point Materials For Training

## Slide 2: Chapter 1 Basic Knowledge About Vehicle-type Construction Machinery

## Slide 3: Types and Models of Vehicle-type Construction Machinery (Leveling, Transportation, Loading and Excavation) (Industrial Safety and Health Act Enforcement Ordinance Appendix 7)
Classification of vehicle-type construction machinery
Vehicle-type construction machinery (leveling, transportation, loading and excavation
Leveling, Transportation, Loading
Excavation
Tractor construction machinery
Shovel (SHOBERU) construction machinery
Bulldozer
Tractor shovel (SHOBERU)
Scrape dozer
Motor grader
Muck loader
Scraper
Power shovel (SHOBERU)
Drag shovel (SHOBERU) (backhoe)
Clamshell
Dragline
Bucket excavator
Trencher
Page 2 of textbook / Page 5 of auxiliary text

## Slide 4: Leveling, Transportation, Loading Machinery
Page 2 of textbook / Page 5 of auxiliary text
Bulldozer example
Tractor shovel (SHOBERU) examples
Scraper example

## Slide 5: Leveling, Transportation, Loading Machinery
Scrape dozer example
Motor grader example
Muck loader examples
Page 5 of textbook / Page 6 of auxiliary text

## Slide 6: Excavation Machinery
Power shovel (SHOBERU) example
Drag shovel (SHOBERU) examples
Clamshell examples
Page 7 of textbook / Page 8 of auxiliary text

## Slide 7: Excavation Machinery
Dragline example
Bucket excavator example
Trencher example
Page 9 of textbook / Page 9 of auxiliary text

## Slide 8: Terminology for Vehicle-type Construction Machinery 1・・・Work Device
Work Device
Page 10 of textbook / Page 10 of auxiliary text

## Slide 9: Terminology for Vehicle-type Construction Machine 車両系建設機械に関する用語2・・・Machine body weight 車両系建設機械に関する用語3・・・Machine weight 車両系建設機械に関する用語4・・・Total machine weight
水
油類
Machine body weight
Machine weight
Gross Vehicle Weight
Machine body weight
Maximum loading weight
Water
Oils
Worker
Fuel
Machine weight
Fuel
Oils
Water
Total machine weight
Page 11 of textbook / Page 10 of auxiliary text

## Slide 10: Terminology for Vehicle-type Construction Machiney 5・・・Stability 6・・・Gradeability
Stability
Gradeability
Stability
Page 12 of textbook / Page 11 of auxiliary text

## Slide 11: Terminology for Vehicle-type Construction Machiney 7・・・Average contact pressure
① Crawler type
② Wheel type
Ｗ：Total machine weight（ｔ）
Ｓ：Total contact area＝2Ｂ×Ｌ（㎡）
Ｌ：Center distance（ｍ）between Idler （idle wheel）and sprocket（sprocket wheel）under total weight state.
Ｂ：Crawler width（ｍ）
Average contact pressure
Average contact pressure
Axial load
Apparent ground contact area
Axial
load
Apparent
ground
contact area
Tire
Ground
Crawler
Idler
Sprocket
Page 13 of textbook / Page 11 of auxiliary text

## Slide 12: Chapter 2 Motors and hydraulic systems for vehicle-type construction machinery

## Slide 13: Motor
Comparison between diesel engine and gasoline engine
Type Item | Diesel Engine | Gasoline Engine
Fuel type | Diesel Fuel | Gasoline
Ignition Method | Self-Ignition by compression of air | By electric spark
Engine mass per horsepower | Heavy | Light
Price per horsepower | High | Cheap
Thermal efficiency | Good (30~40%) | Bad (22~28%)
Operating expenses | Low | High
Risk of fire | Low | High
Page 16 of textbook / Page 12 of auxiliary text

## Slide 14: Diesel Engine Structure
吸・排気装置の例
潤滑装置系統の例
Page 18 of textbook / Page 12 of auxiliary text
Oil cooler
Oil
pump
Lubrication system example
Oil strainer
Oil filter
Intake/ exhaust device example
Muffler
Supercharger
Pre cleaner
Exhaust pipe
Turbine impeller
Proa impeller
Air cleaner
Dust indicator
Cylinder head
Exhaust manifold
Cylinder block
Piston
Pressurized air
Exhaust

## Slide 15: Diesel Engine Structure
Fuel System Example
Water-cooled Engine Example
Page 19 of textbook / Page 13 of auxiliary text
Fuel injection
nozzle
Fuel tank
Fuel injection
pump
Fuel filter
Fuel supply
pump
Governor
Radiator
Thermostat
Water pump
Coolant temperature gauge
Water manifold
Cylinder head
Cylinder liner
From the oil pump (oil)
Engine oil cooler
Fan

## Slide 16: Diesel Engine Structure
Electric Circuit Example
Page 20 of textbook / Page 13 of auxiliary text
Battery relay switch
Battery
Regulator
Fuse box
Lamp switch
Horn
Horn switch
Horn relay
Oil filter
Caution lamp
Heater signal
Safe relay
Panel Lamp
Heater Plug
Start Switch
Head Lamp
Tail Lamp
Working Lamp
Starting motor
Amperemeter
Charging Generator

## Slide 17: Fuel / Engine Oil
An engine oil has the following functions:
① Lubrication
② Cooling
③ Sealing
④ Cleaning
⑤ Rust prevention
Although there are many different brands for engine oil, it is necessary to use the standard brand specified in the instruction manual of the construction machine.
Page 22 of textbook / Page 13 of auxiliary text

## Slide 18: Hydraulic System
Page 24 of textbook / Page 14 of auxiliary text
Engine
High pressure
hydraulic oil
Hydraulic control valve
(Control hydraulic oil pressure and flow direction)
High pressure
hydraulic oil
Low pressure
hydraulic oil
Low pressure
hydraulic oil
Low pressure
hydraulic oil
Hydraulic pump
(Pump out hydraulic oil at high pressure)
Hydraulic oil tank
Auxiliary
Hydraulic drive
(Convert oil pressure into mechanical energy )
Work
(Size / Speed/
Direction )

## Slide 19: Hydraulic Pump ① Gear Pump ② Piston Pump, Inclined Shaft Type, Swashplate Type
Inclined Shaft Type Swashplate Type
Overview of the gear pump operating principle
Hydraulic oil discharge port
Hydraulic oil
suction
port
Swash plate
Cylinder block
Piston
Valve plate
Axis
In/
Out port
Shaft
Piston
Cylinder block
Drive flange
Valve plate
Page 25 of textbook / Page 14 of auxiliary text
In/
Out port
In/
Out port
In/
Out port

## Slide 20: Hydraulic Oil Tank
Hydraulic Oil Tank
Combination Air Breather
Pipe Line Filter
Page 30 of textbook / Page 14 of auxiliary text
Oil level gauge
Air breather
Filter
From the circuit
Strainer
Trap
To the pump
Cap
Air filtration element
Oil
filtration element
Element
Exit
Magnet
From the operation valve

## Slide 21: Chapter 3 Equipment Structure Related to Running of the Vehicle-type Construction Machinery

## Slide 22: Crawler Tractor
Page 35 of textbook / Page 15 of auxiliary text
Crawler Type Tractor Structure Example
Radiator
Engine
Power shift mission
Crawler
Recoil spring
Sprocket (drive sprocket)
Carrier roller
(upper rotary shaft)
Track roller
(lower rotary shaft)
Truck frame
Idler
(take up tumbler)
Final decelerator
Steering clutch
Transverse
Fuel tank
Hydraulic oil tank
Torque converter
Shift lever

## Slide 23: Crawler Tractor
Direct Drive Type Power Transmission Device Example
Engine
Steering clutch
and brake
Bevel gear
Final drive
Direct transmission
Flywheel main clutch
Universal joint
Power Shift Type Power Transmission Device Example
Engine
Steering clutch
and brake
Bevel gear
Final drive
Power shift transmission
Torque converter
Universal joint
Page 35 of textbook / Page 15 of auxiliary text

## Slide 24: Wheel Tractor
Torque Converter Type
Power Transmission Example
HST (Hydro-Static-Transmission) Type
Power Transmission Example
Page 47 of textbook / Page 16 of auxiliary text
Engine
Engine
Engine
Tire
Tire
HST pump
HST motor
Transmission
Differential
Tire
HST motor
(variable capacity type)
HST pump
(variable capacity type)
Transmission
Torque converter
Power Shift Transmission
Differential
Final Drive
Tire
Torque converter
Power shift transmission
Engine
Final drive
Tire
Tire
Differential
Final drive

## Slide 25: Wheel Type Tractor/ Tire
Tire Air Pressure
Page 53 of textbook / Page 17 of auxiliary text
When the Air Pressure is Too Low
When the Air Pressure is Too High
Tires are crushed, heat due to deflection is severe, causing peeling.
Both ends of the tire touch the ground and this part wears quickly.
On hard roads, resistance increases and traction decreases.
Only the center part of the tire touches the ground, and this part wears quickly.
In soft areas, the tire digs deep into the soil and reduces traction.
Even small rocks' edges can easily damage the tire.

## Slide 26: Hydraulic Shovel (SHOBERU) System Construction Machinery （Crawler Type）
Hydraulic Shovel Construction Machinery Hydraulic Circuit Example
Crawler Type Running Operation Device Example
Page 57 of textbook / Page 18 of auxiliary text
Swivel joint
Sprocket
Crawler shoe
Controller Cable
Sprocket
Traveling motor (left)
Traveling motor
Direction Selection Valve
Traveling operation lever
Traveling lever
Backward
Forward
Neutral (N)
2-speed switch
Pedal
Front Idler
Traveling motor

## Slide 27: Motor Grader
Motor Grader Structure Example
Movement of the Front Axle Example
Up And Down Swing Example
Page 63 of textbook / Page 19 of auxiliary text
Differential Gear
Final Drive Section
Wheel Brake
Fuel Injection Pump
Transmission
Engine
Radiator water injection port
Radiator
Pre-cleaner
Blade elevating (left) lever
Circle rotation lever
Circle traverse feed lever
Scarifier elevating lever
Blade elevating (right) lever
Blade traverse feed lever
Leaning lever
Articulate lever
Blade elevating cylinder
Hydraulic motor
Scarifier elevating cylinder
Yellow revolving lamp
Circle
Blade tilt link
Circle rotating machine
Blade traverse feed cylinder
Blade
Scarifier
Front wheel tilt cylinder
Wheel

## Slide 28: Scraper
Motor Scraper Structure Example
Page 66 of textbook / Page 20 of auxiliary text
Yoke
Hitch
F fuel tank
F engine
Steering cylinder
Apron cylinder
Bowl cylinder
Apron
Bowl
Ejector
R Suspension oil tank
R Torque flow transmission
Hydraulic oil tank
R Torque converter
R Output shaft
R Engine
R Fuel Tank
R Differential gear
R Suspension Cylinder
R Wheel Brake
R Final decelerator
R Suspension Arm
Ejector Cylinder
F Suspension oil tank (left)
F: Front
R: Rear
F Torque flow transmission
F Torque flow converter
F Suspension Arm
F Suspension Cylinder
Follow up link
Frame
Steering Oil Tank

## Slide 29: Chapter 4 Handling Equipment Related to Driving Vehicle-type Construction Machinery

## Slide 30: Handling the Start of Driving
(1) Before starting the engine
(2) Start the engine
(3) After starting the engine
Page 69 of textbook / Page 21 of auxiliary text

## Slide 31: Handling While Driving
(1) Start
(2) Driving
Points to keep in mind when climbing up a hill
Check the orientation of the machine when moving forward or backward
Points to keep in mind when turning at high speed
Page 72 of textbook / Page 23 of auxiliary text

## Slide 32: Handling While Driving
(3) Climbing / descending, etc.
(4) Stop running
Points to keep in mind when overcoming obstacles
Using road boards in soft areas example
Stopping on a slope example
Stop on a slope example
Page 74 of textbook / Page 25 of auxiliary text
Careful
Careful
Slowly
Slowly
Shift lever
Idling around 5 minutes
Brake pedal Lock
Clutch
Lever

## Slide 33: Handling of Parking (Parking a Machine)
Points to keep in mind when parking
Grease, oil, etc.
1・・・Grease
2・・・Antifreeze
3・・・Oil
Page 76 of textbook / Page 27 of auxiliary text

## Slide 34: Chapter 5 Structure and Type of Equipment Related to the Work of Vehicle-type Construction Machinery

## Slide 35: Structure and Type of Work Equipment for Tractor-type Construction Machinery
Hydraulic Operation of Crawler Type
Tractor Shovel (SHOBERU) Example
Angle Dozer Example
Straight Dozer Example
Rake Dozer Example
Side frame
Lift shilling
Lift arm
Bucket
Tilt rod
Page 79 of textbook / Page 29 of auxiliary text
Dump (DANPU) cylinder

## Slide 36: Structure and Type of Work Equipment for Tractor-type Construction Machinery
U Dozer Example
Trimming Dozer Example
Ripper Example
Wetland Bulldozer Example
Push Dozer Example
Tractor Shovel (SHOBERU) Example
Page 82 of textbook / Page 31 of auxiliary text

## Slide 37: Safety Devices, etc.
リフトアームの安全ピン等の例
転倒時保護装置の例
1・・・Headlight
2・・・Alarm device
3・・・Head guard and fall protection device (ROPS)
Fall Protection Device
Example
Lift Arm Safety Pins, etc
Example
Page 85 of textbook / Page 33 of auxiliary text

## Slide 38: Structure and Type of Work Equipment for Shovel-type (SHOBERU) Construction Machinery
Work Equipment For Hydraulic Shovels (SHOBERU) Example
Mechanical Clamshell Work Equipment Example
アームシリンダ
ブーム
ブームシリンダ
アーム
バケットシリンダ
ストラップ
ストラップロッド
ドラグショベル用バケット
ドラグ・ショベル
アーム
アームシリンダ
ブーム
ブームシリンダ
バケットシリンダ
ストラップ
ストラップロッド
パワーショベル用バケット
Power shovel (SHOBERU)
タグライン
開閉ロープ
支持ロープ
Tag line
rope
Shell
爪
Shaft
main
Counter
weight
Opening and
closing rope
Arm
Bed
Page 86 of textbook / Page 35 of auxiliary text
Arm cylinder
Arm
Arm cylinder
Arm
Boom cylinder
Boom cylinder
Boom
Boom
Bucket cylinder
Bucket cylinder
Strap
Strap
Strap rod
Strap rod
Bucket for power shovel (SHOBERU)
Bucket for drag shovel
Support rope
Opening and closing rope
Tag line
Nail
Drag shovel (SHOBERU)

## Slide 39: Safety Devices, etc.
Swivel Parking Brake Example
Boom Fall Prevention Device Example
Boom Undulation Stop Device Example
Lock Lever Example
When getting on
and off
(lock operation)
When working (unlocking)
Standard
position
Lock
Free
Turning lever
Switch
Timer
Solenoid valve
Turning motor
Battery
Control pump
Engine
Hydraulic oil tank
Back
stop
Boom
A frame
Off place
Boom hoisting
position
Bolt length
Operation
accuracy
adjustment
Stop bolt
Boom
80°
Page 90 of textbook / Page 36 of auxiliary text

## Slide 40: Motor Grader
Scarifier Device Example
Blade Device Example
Operation Of Motor Grader Work Equipment Example
Spheric Joint
Drawbar
Circle
Blade
Rotating gear chamber
Lifting arm
Lifting link
Traverse feed gear chamber
Blade tilt link
Blade rotation
Leaning
Blade up and down (right)
Blade up and down (right)
Drawer horizontal feed
Page 92 of textbook / Page 38 of auxiliary text

## Slide 41: Scraper
Scraper Work Equipment Example
Muck Loader
Work Equipment For Transfering Loader Example
Yoke
Apron arm
Ejector
Bowl
Apron
Cutting
Edge
Bowl cylinder
Conveyor
Boom
Cylinder
Arm
bucket
Turning frame
Page 94 of textbook / Page 39 of auxiliary text

## Slide 42: Chapter 6 Handling Equipment Related to the Work of Vehicle-type Construction Machinery, etc.

## Slide 43: Bulldozer 1・・・Basic Operation
Bulldozer Operating Device Example
Bulldozer Standard Operation Method
Page 97 of textbook / Page 41 of auxiliary text
(Work lever)
Raise (AGE)
Lower (SAGE)
Float
Left tilt
Right tilt
Driving
seat
Shift lever
forward/
backward
(Steering lever)
Right steering
Left steering
Reverse (acceleration)
Forward (acceleration)
Decelerator Pedal
Brake pedal
Clutch pedal

## Slide 44: Bulldozer 1・・・Basic Operation
PAT Vehicle Angle Posture
Angling Example
Page 99 of textbook / Page 42 of auxiliary text
Angle amount
Straight dozer
Angle dozer

## Slide 45: Bulldozer １・・・Basic Operation
Tilting Example
Cutting Edge Angle Adjustment
PAT Vehicle Tilt Posture
Textbook page 100/ Auxiliary textbook page 42
Tilt amount
Tilting
Brace
Brace

## Slide 46: Bulldozer 2・・・Basic Operation
Driving on a Slope Example
Blade Operation Example
Page 101 of textbook / Page 43 of auxiliary text

## Slide 47: Excavation Work
Ditch Excavation Example
Side Cut Work Example
Slope Drainage Example (NORI MEN HAISUI)
Slot dosing example
Blade height
40～50cm
Side cut work example (a)
Side cut work example (b)
Side cut work example (c)
W
W
W
W
W
①
②
③
①
②
③
④
⑤
⑥
①
②
③
④
W: Water
Page 103 of textbook / Page 44 of auxiliary text

## Slide 48: Dozing (OSHIDO) Operation
溝掘削作業の例
Spreading Work Example
Double Push Example
Relay Pushing Work Example
Parallel Soil Pressing Work Example
Page 105 of textbook / Page 46 of auxiliary text
Double push!

## Slide 49: Embankment (MORIDO) Operation
Embankment (MORIDO) Work Example
Compacting Embankment Work Example
Page 107 of textbook / Page 47 of auxiliary text
(Can be compacted)
(Can be compacted)
(Cannot be compacted)
(Cannot be compacted)

## Slide 50: Finishing Operation
Blade Control Device Example
Rough Finishing Work Example
Finishing Operation Example
Page 109 of textbook / Page 48 of auxiliary text
¼ of blade width
Lower the blade on a surface level
Operate the blade up and down
Fine finish work is
done with a motor grader

## Slide 51: Applied Work
Rooting And Weeding Work Example
Cutting Roots of Bamboo and Bushes Example
Backfilling (UMEMODOSHI) Work Example
Pavement Removal Work Example
Soft Stone Removal Work Example
Rake Dozer
Cut down with a chainsaw in advance
For bamboo and bushes, set the depth to 20 to 30 cm.
Page 109 of textbook / Page 50 of auxiliary text

## Slide 52: Ripper Operation
Single Shank Clipper And Multi Shank Clipper
Soft Ground Shoe Example
Passing Through Soft Ground Example
Downhill Slope And Cross Ripping
Ripper Work In Case Of Rock Mass And Interlocked Grain (SAKAME)
Ripper Work
(1) Rock mass ripping
(2) Interlocked Grain (SAKAME) ripping
Page 112 of textbook / Page 52 of auxiliary text

## Slide 53: Tractor Shovel (SHOBERU)
Tractor Shovel (SHOBERU) Operating Device Example
Page 115 of textbook / Page 56 of auxiliary text
Electronic monitoring system
Direction indicator
Parking brake switch
Work equipment lock switch
Work equipment control lever
Accelerator pedal
Brake pedal
Up and down
shift switch

## Slide 54: Tractor Shovel (SHOBERU)
Lift Arm And Bucket Operation Example
Bucket Height When Driving Example
Page 116 of textbook / Page 56 of auxiliary text

## Slide 55: Excavation Work
Excavation Work Example (1)
Excavation Work Example (2)
Excavation Work Example (3)
Excavation Work Example (4)
Under-mine digging is dangerous
Page 118 of textbook / Page 57 of auxiliary text

## Slide 56: Loading and Transporting Work
Loading Conditions Example (1)
Loading Conditions Example (2)
Loading and Transporting
Work Example
Start loading
Finish
Hinge pin height
Stable
One-sided load
Unstable one-sided load
Unstable
Page 119 of textbook / Page 58 of auxiliary text

## Slide 57: Loading and Transporting Work
Loading and Transporting Work Example V Shift Etc.
掘削作業の例（２）
Throwing Work Example
Low and Carry Method Example
V type (V shift) Work object
Ｉ type (cross shift) Work object
L type (L shift) Work object
T type (T shift) Work object
Note) The movement of the tractor / shovel
At maximum clearance
Loading operation disassembly example
20 cm from eye position
Gradient 0%
Inlet
10%
Page 121 of textbook / Page 59 of auxiliary text
Although the ground is even, it is prohibited to turn it without considering the place.
In general, the turning place on a flat bench should be near the face when loading, and in principle, turn near the loading port when heading for the face after loading.
The bench is usually transported backward to prevent spillage on benches with upslope toward the face (downslope toward the inlet.
Select an even place as much as possible for the turning place, and depending on the bench's condition, it is often the case that the turning place is near the inlet).
On a bench with a downward slope toward the face (upward slope toward the inlet), turns near the face during transportation, and when returning, turns by selecting an even place in the area depending on the presence or absence of spillage.
Even if the distance between the slot and the face is short, turn as described above.
Turning on a bench with downward slope
(Inlet)
(Face)
Cross section
Loading
Transport (forward)
Return (backward)
Feed
Turning on a bench with upward slope
(Inlet)
(Face)
Cross section
Transport (backward)
Return (forward)
Feed
Turn
Turning on an even bench
(Inlet)
(Face)
Transport (forward)
Return (forward)
Feed
Turn
Loading

## Slide 58: Hydraulic Shovel (SHOBERU) (backhoe)
Page 123 of textbook / Page 62 of auxiliary text
Hydraulic Shovel (SHOBERU) Operating Device Example
Arm push
Arm pull
(Left lever)
Left turn
Right turn
Operation lever
Boom Down
Boom Up
(Right lever)
Bucket Dump
Bucket
Excavation
JIS Standard Operation Method
Right operation lever
Boom Down
Boom Up
Bucket
Dump
Bucket
Excavation
Driver seat
Forward
Travelling lever (pedal)
Backward
Right Travelling
lever (pedal)
Left Travelling
lever (pedal)
For 2 Lever (pedal) crawler type
Left operation lever
Arm push
Arm pull
Left turn
Right turn

## Slide 59: Hydraulic Shovel (SHOBERU) (backhoe)
Basic Work With A Hydraulic Shovel (Backhoe) Example
(c) Cut-out finish of slope (NORIMEN)
(d) Groove excavation
(a) Ditch, foundation excavation for buildings
(b) Shallow excavation of the ground surface
Page 123 of textbook / Page 63 of auxiliary text
Climbing and Descending Points
(a) Climbing Points
(b) Downhill Points
Raise the bucket at this point
Return at this point
Return
Drop the bucket as much as possible
Return the bucket
Return at this point
Raise the bucket at this point
Climb down without changing the bucket position

## Slide 60: Excavation Work
Most Efficient Drilling Range With Arms
Orientation Of Crawlers When Excavating On The Shoulder
Basic Work With A Hydraulic Shovel (SHOBERU) (Backhoe) Example
Page 126 of textbook / Page 65 of auxiliary text
Arm cylinder
Arm
Bucket cylinder
Cutting edge angle
Bucket cylinder
Link

## Slide 61: Loading Work
Loading Work Example (1)
Loading Work Example (2)
Loading Work Example (3)
Loading Work Example (4)
Loading Work Example (5)
Telescoping Example
Long Arm Example
Page 128 of textbook / Page 66 of auxiliary text
Reduce the
Turning angle
Keep this gap
Dump

## Slide 62: Hydraulic Shovel (SHOBERU) (loading shovel)
Upper Excavation Work Considering
Drainage Example
Translation Excavation Work Example
Straight Excavation Work Example
Lower Excavation Work Example
Page 131 of textbook / Page 69 of auxiliary text
Make the turn angle as small as possible
Predetermined surface
Coming
Leaving
Slope
Under surface
Slope width
Excavation surface
Appointed under surfacec

## Slide 63: Hydraulic Shovel (SHOBERU) (loading shovel (SHOBERU))
Side Hill Bench Cut Method Example
Box Type Bench Cut Method Example
Page 133 of textbook / Page 71 of auxiliary text

## Slide 64: Hydraulic Shovel (SHOBERU) (loading shovel (SHOBERU))
Page 133 of textbook / Page 72 of auxiliary text
Loading Soil With A Loading Shovel Example
a) Dump (DANPU) on the same ground
b) Loading into a car in a high position
c) Throw the removed soil on top of the dump (DAMPU) pile
d) Loading with belt conveyor
e) Sideways or rear soil dumping (DANPU SURU)
Bucket Cutting Angle
a) Large cutting angle
b) Small cutting angle

## Slide 65: Clamshell
Working With Clamshells Example
Page 136 of textbook / Page 74 of auxiliary text
d) Loading into a container that is in a high place
a) Root cutting of construction site
b) Stockpile
c) Loading into a dump (DANPU) truck

## Slide 66: Dragline
Boom Limit angle
Excavating and Loading Work By Dragline Example
Page 137 of textbook / Page 76 of auxiliary text
Usually, 30 °
or more
(a) Underground slope excavation
(b) Root cutting of building foundation colecting aggegate
(d) Loading on the same surface on the ground
(e) Waterways, ditches, dredging
(e) Loading below the work area
(e) Loading into the hopper

## Slide 67: Motor Grader 1・・・Basic Operation
Motor Grader Operating Device Example
Blade Edge Angle
Scarifier Cutting Angle
Soil Quality and Angle
Page 140 of textbook / Page 77 of auxiliary text
Soil
Quality
Angle degree (θ）
Soil ​gathering
Finishing
Hard soil
Soft soil
Angle degree
Cutting angle adjustment mounting bolt
Cutting angle
Plaid
Plaid blade edge angle
Scarifier lift
Circle sideways feed
Circle rotation
Plaid up and down (left)
Plaid up and down (right)
Plaid seideways feed
Leaning
Articulate
Push
Pull
Push
Pull
Push
Pull
Push
Pull
Push
Pull
Push
Push
Push
Pull
Pull
Pull

## Slide 68: Motor grader 2・・・Basic Operation
Leaning Operation
Blade Contact Example
Tire Leaning For Left Turn
Page 142 of textbook / Page 79 of auxiliary text
(a) Contact between front wheel and plate
(b) Rear wheel and plaid, plaid and frame contact
(c) Blade and scarifire
contact
Direction of travel
due to load
Direction of travel
By leaning
Straight
Turn left
Windrow
Tire leaning direction

## Slide 69: Adaptation Work
Shoulder Reach Posture Example
U-turn At Articulate
Bank Cut Position Example
Working With Snow Plows Example
Offset Traveling
Scarifier Cutting Angle
Page 144 of textbook / Page 79 of auxiliary text
Offset amount
Offset posture using articulate
Cutting angle
Snowplow

## Slide 70: Scraper (Motor Scraper)
Be careful of derailing due to centrifugal force
Be careful not to raise the bowl too much
Scraper Operating Device Example
Basic Excavation Work Example
Soil Removal Work Example
Excavation Sequence Example
Page 147 of textbook / Page 82 of auxiliary text
Start loading
End of Loading
Average excavation depth
Average excavation depth
Bowl too high
Bowl lowering width
Bowl raising width
Bowl operation time
Apron operation
Average excavation depth
End of Loading
Start loading
Too much soil in front of the apron
Do it through
Excavation depth is not fixed
Bowl lowering time is too early
Bowl raising time is too late
Bowl is too wide
Brake pedal
Accel pedal
Hold pedal
Differential lock pedal
Shifting lever
Bowl operation lever
Apron operation lever
Ejector operation lever

## Slide 71: Scraper (Towed Scraper)
In terms of driving, the basic operation is the same as the bulldozer in 6.1.1.
Bulldozer Operating Device Example
Working Status of Towed Scraper
Page 150 of textbook / Page 85 of auxiliary text

## Slide 72: Crawler Type Muck loader Machine
The crawler type muck loader mainly includes a large tractor shovel 6.1.2. and a scraping type loader. This page will describe the scraping type loader.
Operation Device For Scraping Loader Example
Page 154 of textbook / Page 86 of auxiliary text
Arm and turning operation
Crawler (left) operation
Crawler (right) operation
Boom and bucket operation
Bucket setting and up and down conveyor operation
Driving seat
Conveyor driving operation
Hydraulic interlock

## Slide 73: Transfer of Vehicle-type Construction Machinery
Claw Climbing Equipment Example
Relationship between the weight of the loading machine and the climbing equipment example
Use Of Climbing Equipment Example
Loading Position
Use Of Foot Stall Example
Fixed To Trailer Example
Page 157 of textbook / Page 88 of auxiliary text
Mass of loading
machine (t)
Number of climbing tools
Number
Material
Aluminum alloy
Aluminum alloy
Aluminum alloy
Shape dimensions
Length x height x width
Trailer back
Climbing equipment
15° or less
Center of the pitch and center of the crawler
Crawler
Climbing equipment
Vehicle loading
platform
Vehicle loading platform and loading machine’s center line
Foot stall
Stop
Wire
robe
Wire
robe
Pad (packing material)
Lever
block
Wooden block
Oil pressure hose
Blade
Wire robe
Lever block
Drag
Drag
U frame
Pad (packing material)
Drag
Wire robe

## Slide 74: Chapter 7 Inspection and Maintenance for Vehicle-type Construction Machine

## Slide 75: Related Laws, General Precautions
Related Laws
*It is not stated in the law but it is best to store the inspection result as long as machine is in use.
Points to remember when inspecting, etc.
Page 163 of textbook / Page 92 of auxiliary text
Restricted Area during inspection
(Unified safety sign for construction disaster prevention-Example of foreign language display-)
Inspection Classification | Article | Enforcer・Qualifications | Inspection Table Retention Period
Inspection before starting operation | Industrial Safety and Health Act (ISHA) Art. 170 Art. 171 | Driver/ Operator | *As long as machine is in production
Regular Independent Inspection (Once per month) | ISHA Art. 168, 169 ,171 | Person instructed by Business Operator (Safety Manager) | 3 years retention
Specific Independent Inspection (Once per month) | ISHA Art. 167, 169, 169 Par. 2, 171 | In-company inspector Inspection Company | 3 years retention (with inspected mark)

## Slide 76: Daily Maintenance Points Before Starting Engine
How to Discern Hydraulic Oil
Examples of orientation during refilling or inspection
When adjusting the electrical system, remove the minus (－) terminal of the battery.
Page 164 of textbook / Page 94 of auxiliary text
Tire Inspection
Appearance | Smell | Cause
Change to Opaque White | Good | Contamination with other fluids
Change to Dark Brown | Pungent | Deterioration
Has small black dots | Good | Contamination of foreign materials
Bubbling/ Foaming | --------- | Contaminated with grease
Boom
Arm

## Slide 77: Daily Inspection Points After Starting the Engine
Emission Color and Criteria
Page 170 of textbook / Page 94 of auxiliary text
Clutch Adjustment
Operation Inspection
Points during Storing
Emmision Color | Criteria for Inspection
Black | Concentrated vapor, Defective combustion
Faint Yellow | Thin vapor
White/ Blue | Burnt oil, faulty timing
Ash Gray | Concetrated vapor and Burnt oil
No Color | Adequate Vapor, Full combustion
A: Height of Pedal attachment
B: Floor board gap
C: Backlash
A-B-C: Step on it

## Slide 78: Inspection Points When Malfunctions Detected During Operations
If during the operation the construction machine feels that it may have a trouble,
it is necessary to immediately stop the machine on a flat place,
report the faulty area to the responsible officer,
repair the part before going back to operation.
Page 172 of textbook / Page 98 of auxiliary text

## Slide 79: Chapter 8 Safety Driving Guidelines, Cue Signs, and Guiding

## Slide 80: Safety Driving Guidelines
Page 175 of textbook / Page 99 of auxiliary text
Turn off engine when leaving the vehicle
Check the situation of inspection

## Slide 81: Signals and Guiding Points
<Signal with Whistle> <Signal using Voice>
• Safe：2 Short blows repeatedly • Safe：All right, All right (ORAI, ORAI)
• Stop：Long whistle blow • Stop：STOP (SUTOPPU)
Page 179 of textbook / Page 101 of auxiliary text
The inductor must wear clothes that is visible and stand in a location where the driver of machinery can see at ease.

## Slide 82: Chapter 9 Force and Electricity Knowledge

## Slide 83: Moment of Force
Page 181 of textbook / Page 102 of auxiliary text
Moment of Force
Moment of Fall
Length until Bucket l1
Fulcrum
Body Mass W0

## Slide 84: Mass and Specific Gravity
Page 188 of textbook / Page 103 of auxiliary text
Object Unit Weight
Volume Formula Chart
*Wood mass is dry mass. Soil, gravel, sand, lime and cork are appearance unit weight.
Object Mass＝ Volume × Specific Gravity
Material type
Lead
Copper
Steel
Cast Iron
Aluminum
Concrete
Soil
Gravel
Sand
Coal (powder)
Cokes
Oak
Pine
Cedar
Cypress
Paulownia
Material type
Mass per 1m3 (t)
Mass per 1m3 (t)

## Slide 85: Center of Gravity, Object Stability（Suwari）
Page 189 of textbook / Page 104 of auxiliary text
How to find Center of Gravity
Center of gravity
Object Stability
Center of gravity right on top of the object thus stable
Derived from center of gravity right
Derived and loose thus dangerous
Stable
Center
Unstable
Stable
Stable

## Slide 86: Object Movement
Page 194 of textbook / Page 105 of auxiliary text
Static Friction
Centrifugal Force /Centripetal Force (b)
Falling through Centrifugal Force
Velocity and Acceleration
Centrifugal Force /Centripetal Force (a)
Object A
Center (Hand)
Centripetal
Centrifugal
Non-constant velocity movement
Constant velocity movement

## Slide 87: Electrical Knowledge
Page 202 of textbook / Page 109 of auxiliary text
Reaction when electric current passes human body Unit mA (Milliampere)
Note) 1 mA is equal to 1/1000 A (Ampere)
Shock Effect | Alternate Current (AC) |  | Direct Current (DC) | 
 | Male | Female | Male | Female
1.Tingling Sensation | 1.1 | 0.7 | 5.2 | 3.5
2. Shock with pain (but still able to move muscles) | 9.0 | 6.0 | 62.0 | 41.0
3. Shock with pain (with muscle stiffness, and shortness of breath) | 23.0 | 15.0 | 90.0 | 60.0
4. Often causes death instantly | 100 |  | 100 | 

## Slide 88: Electrical Knowledge
Page 203 of textbook / Page 109 of auxiliary text
Offest Distance from Power Transmission and Distribution Wire
(Power Line)
High voltage power line
Safety
Safety
Safety
Safety
(Power Line)
High voltage reduction wires
Low voltage wires
Safety
Vehicle road
Housing side
Pole Transformer
(Be careful with high voltage wire when reaching transformer )
Safety
Safety
Extra high voltage
Most of the transmission lines are steel towers but there also cases where it is using poles; thus, caution is needed.
Offset distance
Safety
Attention
Overhead ground wire
Transmission line

## Slide 89: Chapter 10 Topography and Construction Knowledge

## Slide 90: Rock Chemistry, Soil
Page 207 of textbook / Page 111 of auxiliary text
Classification of Rock Hardness
Particle Diameter Classifications and Terms
Compact Land Composition
Classification | Compression Rate (N/mm2) | Elastic Wave Velocity(km/s) | Rock Type Examples
Soft-rock | 10 | Below 1.5 | Tertiary Pelitic Rock, Partial Sandstone
Medium-hard rock | 10~50 | 1.5~3.0 | Majority of Tertiary Sedimentary Rock
Hard rock | 50~150 | 3.0~5.0 | Mesozoic/Paleozoic era Pelitic Rock
Superhard rock | 150 and up | 5.0 and above | Chert, Hard sandstone, Gabbro, Igneous rock like Diabase, Gneiss, Quartz Schist, Hornfels
Water and Air
Water and Air
Natural soil
Compacted finished
Compacted
Load weight
Load weight
Sand
Fine Sand
Coarse Sand
Fine Gravel
Coarse Gravel
Medium Gravel
Gravel
Particle Diameter
Clay
Silt

## Slide 91: Land Composition
Page 212 of textbook / Page 112 of auxiliary text
Land Composition
Air
Water
Soil Particle
Solid (Soil Particles)
Gap (Gas,
Liquid)
Full Land Mass
Soil Particle Mass
Water Mass
Air Mass(=0)
Full Land Volume
Soil Particle Volume
Water Volume
Air Volume
Land Gap Volume

## Slide 92: Foothold Hardness
Page 215 of textbook / Page 113 of auxiliary text
Cone Index
Note）Numbers may change depending on soil texture
Machine Type
Cone Index (N/mm2)
Ground Pressure (N/mm2)
Medium size swamp bulldozer
Medium size bulldozer
Large size bulldozer
Scrapedozer
Carryall Scraper
Motor Scraper
Dumptruck
Above
(Bog-type)
(Load Capacity)

## Slide 93: Soil Volume Changes
Page 216 of textbook / Page 114 of auxiliary text
Rate of Change of Soil Volume
Natural ground
Soil volume
Unraveled soil volume
Compacted soil volume
Soil Volume Changes
Gravel
Sand
Hard Rock
Medium-hard Rock
Soft Rock
Rock Lump/Precious Stone
Rock and Stone
Sand mixed with gravel
Sand
Common Soil
Viscous Soil, etc.
Hard Soil
Hardened Hard Soil
Viscous soil
Rock Lump/Sand mixed with precious stone
Sandy Soil
Rock Lump/Sandy soil mixed with precious stone
Viscous soil mixed with gravel
Rock Lump/Viscous soil mixed with precious stone
Name

## Slide 94: Signs and Causes of Sand Erosion
Page 218 of textbook / Page 115 of auxiliary text
Reclaimed Slope Surface and Height Basis
Excavated surface’s height ・Slope
Soil Type
Ground made of bedrock or hard clay
Other type ground
Ground made of sand
Ground that easily collapse due to blast, etc.
Over
Or
Less
Less
Over
Less
Less
Or
under
under
under
Over
under
Less
Over
under

## Slide 95: Signs and Causes of Sand Erosion, Land Strength, Signs of Landslides
Page 218 of textbook / Page 116 of auxiliary text
Examples of Landslide on Upright Slope
Slope Landslide Examples
Signs of Landslide
Rock Collapse Pattern
Soil Collapse Pattern
Granite soil
Weathered residual rock lump
Weathered granites
(layered structure like an onion)
Terrace gravel layer
(Conglomerate type)
Cliff cone deposit
(cliff cone type)
Boulder type rockfall (falling type)
If the filling inside the gravel layer (matrix) is made of a material with a low degree of solidification, such as rock mass or boulder, weathered and eroded, the boulder will float and lose its balance. It's a type that collapse.
It is a type in which the rock mass separated by the crack is flaked along the crack.
It's a medium-scale collapse that collapses along the rock joints. Excavation can open potential cracks, where rainwater, etc., percolate and weaken the ground, and often collapse along a straight line on the slide surface.
Stress is released by the excavation of soil and earthen ground, and weathering progresses, and it absorbs water and collapses due to subsequent rainfall, etc., and is the most common type of ground collapse.
It is a type of collapse caused by the development of an extremely low-strength weak line in the bedrock, and the soil layer slips down along that line. The avalanche scale depends on the relationship between the slope and the weak line, inclination, etc. The scale of collapse is determined by the relationship between the slope and the weak line, the inclination angle, and so on. Also, the tip may protrude out.
Fragmented rock type rockfall (abrasion type)
Rock with lot of crack
Rock with lot of crack
Hardness alternating layer
Rocks with columnar joints
Rock separation/break down type collapse
Soft rock or soil
Unconsolidated soil
Debris flow
Spring water
Permeable layer
Impermeable layer
Colluvium or topsoil
Collapsed soil avalanche
Clay layer
Composite slide
Viscous soil arc slide
Large scale collapse (land slide type)
Large scale collapse (rockslide)
Stratum, joint dip slope
Dislocation, dike
Joint dip slope
Fault fracture zone or surface of separation
Bedding, slide plane
Rock mass falls in the range of one or several rock (rockfall type) Type I
Surface collapse is shallow, small-scale collapse (detachment type/breakdown type) Type II
Collapse surface is deep or widespread Type III
Presence of impermeable layer
Soil shedding, breakdown type collapse
Rock hardness alternating layer

## Slide 96: Excavation Methods
Page 224 of textbook / Page 119 of auxiliary text
Island Construction Method
Open Cut Grading Works Example
Top of slope
Slope inclination
Slope curing
Sandbag
Toe of slope
Berm
Drain Gutter
Drain Gutter
Excavation bottom surface
Earth retaining wall
Strut
Waling

## Slide 97: Excavation Methods
Page 226 of textbook / Page 119 of auxiliary text
Open Cut Binder Construction Method Example
Mortar
(c) Earth anchor method
Steel rod or PC steel wire
Tie rod
Anchor
Tie rod method
Earth retaining wall
Self sustaining method
Construction
Embedment part
Timbering
Waling
Bracket
Middle block
Middle block
Earth retaining wall
Strut
Strut

## Slide 98: Excavation Methods
Page 227 of textbook / Page 120 of auxiliary text
Inverted Lining Example
Trenchcut Construction Method Example
Earth retaining wall
Earth surface
First
2nd
3rd

## Slide 99: Chapter 11 Accident Case

## Slide 100: Casualties Disaster in the Construction Industry
Page 121 of auxiliary text
Changes in the construction industry’s fatal accidents with four or more of business closure as shown by figure 11-1
図１１－１ 建設業における休業４日以上の死傷災害の推移
(Excludes those directly caused by the Great East Japan Earthquake)
In addition to the fatal accidents that occurred in 2017 caused by construction machinery, about 56% is caused by leveling, transportation, loading, and excavation machinery, and 15% is caused by demolition machinery.
(Reference) Occupational Accident Occurrence Status, Workplace Safety Site: Analysis of Occupational Accident Cause Factors (2017, Construction Industry) by The Ministry of Health, Labor and Welfare.
Case number (person)

## Slide 101: E.g., 1． The construction worker was caught between drag shovel (SHOBERU) counterweights
Page 230 of textbook / Page 122 of auxiliary text
E.g., 2．
While leveling the soil with the drag shovel (SHOBERU), the operator was caught between strut and lever.
E.g., 3． Blocks from the drag shovel (SHOBERU) bucket fell on a worker.
E.g., 4． The drag shovel (SHOBERU) was overturned on a slope and crushed the guide beneath it.

## Slide 102: E.g., 5 A worker was hit by a turning bucket when he was walking in front of a drag shovel (SHOBERU).
Page 234 of textbook / Page 126 of auxiliary text
E.g., 6 After finishing the inspection of the bulldozer, while installing the cover, the worker lost his balance and his foot got caught.
E.g., 7 The buldozer fell down the slop and the driver was squashed by the buldozer.
E.g., 8 A marking worker was caught up by the crawler while the buldozer moving backward.

## Slide 103: E.g., 9 While hanging a load using a tractor shovel (SHOBERU), it crashed into a worker.
Page 238 of textbook / Page 130 of auxiliary text
E.g., 10 At a mine, a guide was caught in the bucket of the showel tractor.
E.g., 11 A construction worker was run over by a moving backward motor grader.
E.g., 12 A scraper fell on a sloping ground and the driver was crushed beneath it.

## Slide 104: Legal system for worker safety and health
Page 134 of auxiliary text
There are several laws regarding to worker safety and health, including the industrial safety and health law. In particular, the industrial safety and health act stipulates matters that must be observed for the purpose of ensuring the safety and health of the workers and promoting the formation of a comfortable working environment. Specific matters associated with the enforcement of the law are indicated in the government ordinances, ministerial ordinances, notifications, etc.
The legal system for worker safety and health are as follows:
Figure 9-1 Vehicle type construction machine (leveling, transport, loading and excavation) legal system for driving skill.
（Reference) Ministry of Health, Labor, and Welfare. Risk assessment for building maintenance industry manual
LAW
CABINET ORDER
MINISTERIAL ORDINANCE
PUBLIC NOTICE/NOTIFICATION
Industrial Safety and Health Act (Safety Act)
Industrial Safety and Health Act Enforcement Ordinance (Safety Ordinance)
Industrial Safety and Health Act Enforcement Regulation (Safety Regulations)
Vehicle type consruction machine standard
Vehicle type construction machine (leveling, transport, loading and excavation) driving skill training rules.
Safety and health special education regulation

## Slide 105: Industrial Safety and Health System（Extract）（１）
Page 243 of textbook / Page 134 of auxiliary text
Chapter 1 General Rule
Article 3 (Responsibility of Business)
Business operators must not only comply with the minimum standards for the prevention of occupational accidents stipulated by this law, but also to ensure the safety and health of workers in the workplace. In addition, business operators must cooperate with the government's measure to to prevent occupational accidents.
2. Anyone who designs and manufactures machine, appliances, and other equipments, or importers, anyone who manufactures raw materials, or importer, or anyone who contsructs or designs the building must endeavour to the prevention of occupational accidents due to the use of these items when designing, manufacturing, importing, or constructing these items.
3. Anyone who orders a construction work, anyone who takes over a work to other party, must follow the construction methods and periods, etc. in order not to impose conditions that may impair the execution of a safe and hygienic work.
Article 4 Workers must comply with necessary matters to prevent occupational accidents and endeavour to cooperate with the measures to prevent occupational accidents implemented by business operators and other related parties.

## Slide 106: Industrial Safety and Health Act（Extract）（２）
Page 248 of textbook / Page 135 of auxiliary text
Chapter 5 Regulations on machinery, etc, hazardous substances
Article 45 (Periodic self inspection)
Business operators must comply with the regulations by the Ordinance of Ministry of Health, Labor and Welfare by carrying out periodic self inspection of boilers and other machinery, etc. specified by the Cabinet order and record the result.
2 When business operator conducts the self-inspection as specified by the Ordinance of Ministry of Health, Labor and Welfare (hereinafter referred to as "specific self-inspection") among the self-inspections under the regulation of the same paragraph for machinery, etc. as specified by the Cabinet Order in the preceding paragraph, workers who use it are those who have the qualifications specified by the Ordinance of the Ministry of Health, Labor and Welfare, or those who have the registration as prescribed in paragraph 1 of Article 54-3. At the request of others, the person who conducts a specific self-inspection of the machine (hereinafter referred to as "operator") must also perform this regulation.
3 The Minister of Health, Labor and Welfare shall publish guidelines necessary for proper and effective implementation of self-inspection in pursuant to the regulation in paragraph 1.
4 Omitted
Table 5-1 related to Laws and Regulations
Inspection Classification | Provision | Implementor /Qualification | Storage Period of inspection table
Inspection Before starting work | Safety Regulations Article 170 171 | Driver | Checklist while the machine is running
Periodic Self-Inspection (Once a month) | Safety Regulations Article 168 169 171 | A person designated by Business operator (Safety Manager) | Inspection table for 3 years
Specific Self-Inspection (Once a year) | Safety Regulations Article 167 169, 169 par 2 171 | In-house inspector Inspection Company Inspector | Inspection table for 3 years (Attach the inspection mark)

## Slide 107: Industrial Safety and Health Act（Extract）（３）
Page 250 of textbook / Page 136 of auxiliary text
Chapter 6 Measures of Workers Employment
Article 61 <Employment Restriction>
Business operators shall operate crane and other operations as specified by the Cabinet Order, i.e., shall only be operated by a person who has obtained a license from the prefectural labor bureau director for the relevant work, or a person who has been registered by the prefectural labor director. Only those who have completed the skill training and those with qualifications specified by the Ordinance of the Ministry of Health, Labor and Welfare shall be allowed to engage in the relevant work.
2 According to the provision of the preceding paragraph, other than the person who can do the appropriate operation, no one shall engage in the appropriate operation.
3 According to the provisions of paragraph 1, when the operator who can engage in the appropriate operation is engaging in the appropriate operation, the operator must carry an appropriate driver’s license or other qualification
4 Omitted
Qualifications required for machinery operator Qualifications required for workers

## Slide 108: Industrial Safety and Health Act Enforcement （Extract）
Page 251 of textbook / Page 136 of auxiliary text
Article 20 (Business with Employment restriction)
The business specified by the Cabinet Order under Article 61 as follows.
1~11 Omitted
12 Work operation of construction with machine body mass of 3 tons or more as listed on the attached table 7 No.1, No.2, No.3, or No.6 can use power and can self-propel in unspecified places
13 below omitted

## Slide 109: Ordinance on Industrial Safety and Health (Extract) (1)
Page 256 of textbook / Page 138 of auxiliary text
Part 1 General Rules
Chapter 7 License, etc.
Section 3 Skills Training Course
Article 82 <Reissuance, etc., of the Skill Training Course Completion Certificate>
A person who has received a skill training course completion certificate and been actually engaging or intends to engage in the work pertaining to the said skill training shall, in the case of loss or damage of the certificate excluding a case prescribed by paragraph (3) below, submit an application document for the reissuance of the skill training course completion certificate (Form No.18) to the registered training institution that issued the certificate, and thereby reacquire the skill training course completion certificate.
2 A person prescribed by the preceding paragraph shall, when having changed the name or, submit an application document for change of the skill training course completion certificate (Form No.18) to the registered training institution that issued the certificate, and thereby revise the certificate excluding a case prescribed by paragraph (3).
3 Omitted below

## Slide 110: Ordinance on Industrial Safety and Health (Extract) (2)
Page 261 of textbook / Page 138 of auxiliary text
Part 2 Safety Standards
Chapter 2 Construction Machine, etc
Section 1 Vehicle Type Construction Machine
Subsection 1 Structure
Article 152 < Providing of Front Lamp >
The employer shall provide a vehicle type construction machine with a front lamp. However, this shall not apply to a vehicle type construction machine used at a place maintaining necessary illumination for carrying out the work safely.
Article 153 < Head Guard>
The employer shall, when using a vehicle type construction machine (limited to a bulldozer, a tractor shovel (SHOBERU), a muck loader, a power shovel (SHOBERU), a drag shovel (SHOBERU) and a breaker) in ※1 a place where it is liable to cause dangers to workers due to falling of rocks, etc., provide the said vehicle type construction machine with ※2 a sound head guards.
Note 1) "A place where there is a risk of falling rocks, etc...." are places where Open-cut excavating work, excavating work for quarrying, construction work of a road, etc. is performed using the machine, and the work by the machine causes the falling of rocks, etc.
Note 2) Regarding the head guard, the structural standard is indicated by Circular No. 559 of 1975.9.26
Subsection 2 Prevention of Dangers Pertaining to the Use of a Vehicle Type Construction Machine
Article 154 <Investigation and Record>
The employer shall, when carrying out the work using a vehicle type construction machine, investigate in advance the landform and condition of the nature of the soil, etc., of the place pertaining to the said work in order to prevent workers from dangers due to falling of the said machine, collapse of natural ground, etc., and record the result of the investigation.

## Slide 111: Ordinance on Industrial Safety and Health (Extract) (3)
Page 262 of textbook / Page 139 of auxiliary text
Article 155 <Work Plan>
The employer shall, when carrying out the work using a vehicle type construction machine, establish in advance a work plan in conformity with what is known by the investigation pursuant to the provision of preceding Article, and carry out the work by the said work plan.
2 The work plan set forth in the preceding paragraph shall be the one describing the following matters:
1 The type and capability of the vehicle type construction machine to be used.
2 The travelling route of the vehicle type construction machine.
3 The work method by the vehicle type construction machine.
3 The employer shall, when having established the work plan set forth in paragraph (1), make the matters set forth in item (2) and (3) of the preceding paragraph known to the workers concerned.
Article 156 <Speed Limit>
The employer shall, when carrying out the work using a vehicle type construction machine (excluding the one having maximum speed of10 km/h or less), in advance, set the appropriate speed limit for the vehicle type construction machine corresponding to ※the landform and conditions of nature of the soil, etc., of the place pertaining to the said work and carry out the work by the set speed limit.
2 The operator of the vehicle type construction machine set forth in the preceding paragraph shall not operate the vehicle type construction machine at speeds exceeding the speed limit set forth in the same paragraph.
Note) "Etc. " in " the landform and conditions of nature of the soil, etc. " includes the case where other machinery and equipment are installed.

## Slide 112: Ordinance on Industrial Safety and Health (Extract) (4)
Page 262 of textbook / Page 140 of auxiliary text
Article 157 < Prevention of Falling, etc.>
The employer shall, when carrying out the work using a vehicle type construction machine, take necessary measures for the travelling route of the said machine etc., such as preventing collapse of shoulder and uneven settling of the ground and maintaining the※1 necessary width etc., in order to prevent workers from dangers due to overturning or falling of the said machine.
2 The employer shall, in the case where the work using a vehicle type construction machine is carried out at road shoulder, inclined place, etc., and when it is liable to cause dangers to workers due to overturning or falling of the said machine, ※2 arrange a guide, and have the said person guide the said machine.
3 The operator of a vehicle type construction machine set forth in the preceding paragraph shall follow the instructions given by the guide set forth in the same paragraph.
Note 1) "Etc. “ in "necessary width etc." includes installation of guardrails, setting of signs, etc.
Note 2) If guardrails are installed and signs are set properly so that there is no risk of falling or falling, it is not necessary to arrange a guide in Paragraph 2.
Article 157-2
The employer shall, must use a vehicle type construction machine are equipped with seat belts and workers must use seat belts, at road shoulder, inclined place, etc., when it is liable to cause dangers to workers due to overturning or falling of the said machine.

## Slide 113: Ordinance on Industrial Safety and Health (Extract) (5)
Page 263 of textbook / Page 141 of auxiliary text
Article 158 < Prevention of Workers Being Hit>
The employer shall, when carrying out the work using a vehicle type construction machine, not allow a worker to enter ※a place, which is liable to cause dangers to workers due to being hit by the vehicle type construction machine during operation. However, this shall not apply to when arranging a guide and having the said person guide the said machine, etc.
2 The operator of the vehicle type construction machine set forth in the preceding paragraph shall follow the instruction given by guide set forth in the proviso of the same paragraph.
Note ) “A place, which is liable to cause dangers to workers” includes not only the traveling range of the machine but also the operating range of the working device such as an arm and a boom.
Article 159 <Signals>
The employer shall, when placing a guide for operation of a vehicle type construction machine, set fixed signals and have the said guide give the signals.
2 The operator of the vehicle type construction machine set forth in the preceding paragraph shall follow the signals set forth in the same paragraph.
Article 160 < Measures to Be Taken in the Case of Leaving the Operating Station>
The employer shall, when the operator of a vehicle type construction machine leaves the operating station, have the said operator take the following measures:
1 To lower a working device of ※1 a bucket, ripper, etc., on the ground.
2 To stop a prime mover and take measures such as ※2 setting the brake ,etc., in order to prevent a vehicle type construction machine from breaking into a run.
2 The operator set forth in the preceding paragraph shall take measures listed in each item of the same paragraph when leaving the operating station of the vehicle type construction machine.
Note 1) "Etc. “ in " a bucket, ripper, etc. " includes shovel, blade, etc.
Note 2) "Etc. “ in " setting the brake ,etc.“ includes stopping with wedges, stoppers, etc.

## Slide 114: Ordinance on Industrial Safety and Health (Extract) (6)
Page 264 of textbook / Page 142 of auxiliary text
Article 161 < Transfer of Vehicle Type Construction Machine >
The employer shall, when using a loading plate, fills, etc., in the case where a vehicle type construction machine is loaded to a truck, etc., or unloaded from a truck, etc., by ※1 self-propelling or towing for transferring the said machine, comply with the following provisions in order to prevent dangers due to overturning, falling, etc. of the said machine:
1 To load or unload at a level and firm place.
When using a loading plate, to use the one with a ※2 sufficient length, width and strength, and fix it securely with ※3 appropriate incline.
When using fills or a temporary stand, etc., to secure a sufficient width, ※4 strength and appropriate incline.
Note 1) "Self-propelling" includes trailer.
Note 2) "Sufficient" of "sufficient length" should be determined according to the weight and size of the vehicle type
construction machine for loading and unloading
Note 3) "Appropriate incline" refers to incline within a safe range in consideration of the performance such as climbing
power of the machine.
Note 4) The “strength of fills“ is secured by striking logs that are difficult to fill and taking measures such as solidifying
them sufficiently.
Article 162 < Restriction of Riding>
The employer shall, when carrying out the work using a vehicle type construction machine, not allow a worker to ride on places other than ※the seat.
Note ) “The seat“ refers to the driver's seat, passenger seat, and other seats for boarding.
Article 163 <Restriction of Use>
The employer shall, when carrying out the work using a vehicle type construction machine, abide stability, the maximum working load, etc., ※ decided on the basis of its structure in order to prevent workers from dangers due to overturning, destruction of working device of an arm or a boom, etc.
Note ) “ Decided on the basis of its structure “ is indicated by the structural standard of vehicle type construction
machine

## Slide 115: Ordinance on Industrial Safety and Health (Extract) (7)
Page 265 of textbook / Page 143 of auxiliary text
Article 164 <Restriction on the Use for Other than Main Purpose>
The employer shall not use a vehicle type construction machine for other than its main purpose of lifting a load by a power shovel (SHOBERU), ※1 raising or lowering a worker by a clamshell, etc.
2 The provisions of the preceding paragraph shall not apply to the following cases:
1 The case falling under all of followings, in the case where the ※2 load lifting work is carried out:
a. When it is ※3 unavoidable due to the nature of the work or necessary for the safe implementation of the work.
b. When metal parts of a hook and a shackle or ※4 any other hoisting parts falling under all of following conditions are fitted to work device such as an arm and a bucket:
(1) To have ※5 sufficient strength corresponding to the load to be burdened.
(2) To be unlikely to cause danger of the load falling from the said parts due to the use of a latch, etc.
(3) To being unlikely to cause coming off from the work device. ※6
2 In the case where works other than lifting a load is carried out, and when
it is unlikely to cause dangers to the workers
Note 1) The "etc." of "raising or lowering a worker by a clamshell, etc." includes the use of a boom, arm instead of a ram
Note 2) "Load lifting work" includes turning the boom with the load and running with the load.
Note 3) "When it is unavoidable due to the nature of the work or necessary for the safe implementation of the work “ in order to reduce the risk of sediment collapse as part of excavation work using vehicle type construction machine, when temporarily lifting earth retaining sheet piles, hume pipes, etc., the work area is narrow, It may be considered that the workplace becomes more complicated, and the danger increases if a mobile crane is carried in and the work is performed
Note 4) "When metal parts of hoisting parts are fitted to work device" means that the hook, shackle, wire rope, hanging chain, etc. are attached to the working device so that they will not come off easily and can be used to lift the load. It does not include cases where a wire rope is hung on the claws of the bucket to lift the load, and cases where the wire rope is turned directly on the boom or arm to lift the load.
Note 5) The strength of the lifting equipment should have a safety factor of 5 or more(The value obtained by dividing the value of the cutting load of the lifting equipment by the value of the load in Paragraph 3, No.4)
Note 6) "To being unlikely to cause coming off from the work device" are those with hooks, attached by welding, which are welded so that sufficient penetration, throat thickness, can be obtained, and welded over the entire circumference of the attachment part.

## Slide 116: Ordinance on Industrial Safety and Health (Extract) (8)
Page 265 of textbook / Page 144 of auxiliary text
Article 165 < Repair, etc.>
The employer shall, when carrying out the work repairing a vehicle type construction machine, or fitting or removing its attachments, designate a person to direct the said work and have the said person take the following measures:
1 To decide a work procedure, and direct the work.
2 To monitor the use of a safety prop, a safety block, etc., prescribed by paragraph (1) of the next Article.
Article 166 <Prevention of Dangers Due to Lowering of a Boom, etc.>
The employer shall, when carrying out the work repairing, checking, etc., under the raised boom or arm, etc., of a vehicle type construction machine, have the worker engaging in the said work use a safety prop, a safety block, etc., in order to prevent workers from dangers due to unexpected descending of the boom or the arm, etc.
The worker engaging in the work set forth in the preceding paragraph shall use a safety prop, a safety block, etc.※, set forth in the same paragraph.
Note ) The "etc." of the "safety block, etc." includes a stand, etc.

## Slide 117: Ordinance on Industrial Safety and Health (Extract) (9)
Page 268 of textbook / Page 144 of auxiliary text
Article 166 -2 <Prevention of Dangers due to Collapse of Attachments, etc.>
The worker engaging in the work must use stand when installing or removing attachments for vehicle type construction machine, to prevent the danger of workers due to the collapse of attachments, etc.
2 The worker engaging in the work set forth in the preceding paragraph must use stand, set forth in the same paragraph.
Article 166 – 3 <Restrictions on Attachment>
The employer shall, not attach attachments to vehicle type construction machine that exceed the structurally specified weight.
Article 166 – 4 <Display of Weight of Attachment, etc.>
The employer must display the weight of the attachment (When a bucket, zipper, etc. is installed, the capacity or maximum load weight of the bucket, zipper, etc. is included. Same in this article below) in a position that is easy for the driver to see when Replaced the attachment of vehicle type construction machine, or equip the document on vehicle type construction machine that driver can easily check the weight of the

## Slide 118: Ordinance on Industrial Safety and Health (Extract) (10)
Page 273 of textbook / Page 145 of auxiliary text
Part 4 Special Regulations
Chapter 2 Special Regulations Concerning Machine Lessor, etc.
Article 666 < Measures to Be Taken by Machine Lessor, etc.>
A person prescribed by the preceding Article (hereinafter referred to as “machine lessors etc.”) shall, when they lease machines, etc., take the following measures:
To check ※1 in advance the said machine, etc., and carry out the repair or other necessary maintenance when having found any abnormalities
To deliver the document indicating the following matters to the employers to whom machines, etc., are leased.
a. The capabilities of the said machines, etc. ※2
b. Characteristic of the said machines, etc., and other matters of the machines, etc., such as precautions for use. ※3
2 The provisions of the preceding paragraph shall not apply to the case that the selection of machines, etc., at the time of their purchase and their maintenance work after the lease which should originally be made by the owner are made by the employer to whom the machines, etc., are leased (including the small-scale enterprise facilities leasing business conducted by prefectural facilities leasing agency prescribed by paragraph (6) of Article 2 of the Act of Financial Aid on Facility Introduction for Small Scale Enterprises [Act No.115 of 1956])※4
Note 1) “In advance" does not necessarily mean to inspect the entire loan each time, but it may be limited to the necessary parts depending on the usage situation.
Note 2) “Capacity of the machine, etc.” refers to the capacity that is particularly necessary for use of using vehicle type construction machine, such as stability and bucket capacity.
Note 3) “Other matters of the machines" refers to matters to be noted when using the machine, such as fuel used and adjustment method.
Note 4) The purpose of Paragraph 2 is not applicable to those that take the form of leasing as a financial means from the purpose of this Article.

## Slide 119: Structural standard of Vehicle Type Construction Machine (Extract)
Page 276 of textbook / Page 146 of auxiliary text
Article 1 < Strength, etc. >
Article 2 < Stability >
Article 3 (Stability of Piling Machine and Punching Machine)
Article 4 (Rear stability of excavation machines (excluding crawler type) and dismantling machines (excluding crawler type))
Article 5 < Brakes for Driving, etc.>
Article 6 < Brake for Work Equipment >
Article 7 <Operating Parts of Traveling Devices, etc.>
Article 8 (Matters necessary for the operation such as the function of the operation part and the operation method)
Article 9 <Visibility Required for Driving , etc. >
Article 10 < Elevating Equipment >
Article 11 < Danger Prevention Equipment by Raising and Lowering Arms, etc. >
Article 12 < Direction Indicator >
Article 13 < Alarm Device >
Article 13-2 < Automatic Stop Device, etc. when the work range is exceeded >
Article 14 < Safety Valves, etc. >
Article 15 < Display >
Article 16 < Vehicle Type Construction Machine with a Special Structure >
Article 17 < Exclusion from Application >