## Slide 1: Shovel Loader Auxiliary Textbook for Driver Technical Training PowerPoint for Training

## Slide 2: Part 1 General Overview

## Slide 3: Chapter 1 Shovel Loader Etc., Overview

## Slide 4: Shovel Loader Etc. Definitions and Characteristics
Figure 1-1 Shovel Loader (without reach mechanism)
Figure 1-2 Shovel Loader (with reach mechanism)
Textbookbook page 13 / Auxiliary Textbook page 4

## Slide 5: Shovel Loader Etc. Definitions and Characteristics
Figure 1-3 Fork Loader
Textbookbook page 14 / Auxiliary Textbook page 5

## Slide 6: Shovel Loader Etc. Definitions and Characteristics
Reference Figure Wheel Loader
Textbookbook (there’s no page) / Auxiliary Textbook page 6

## Slide 7: Main Specifications and Dimensions
Figure 1-4 Bucket
図1－5 Ⅰ型バケット
Textbook page 16 / Auxiliary Textbook page 7
Spill Guard
Bucket Body
Bottom Cutting Edge
Side Cutting Edge
Figure 1-5 I Shape Bucket

## Slide 8: Main Specifications and Dimensions
Table 1－2 Bucket type and characteristics
Figure 1-6 II Shape Bucket
Textbook page 18 / Auxiliary Textbook page 8 - 9
Spill Guard Top Edge
Chevron shaped blade's tip
Consider this imaginary line as the blade's tip front edge
The most common shape bucket with straight edge and no claws. Suitable for handling small size object such as sand, gravel, soil, etc.
The capacity may be increased with the same shape for handling objects with a small relative density. (Specific objects)
Similar to I shape bucket, this type is also suitable for handling small-sized objects. However, in order to increase the scooping ability, the edge is chevron- shaped.
The I shape with straight edge is accentuated with claw and suitable for handling chips with bigger granularity such as crushed stone.
The II shape with chevron edge with claws and is used when need to handle chips with big granularity when improving scooping performance is wanted.
Ⅲ shape
Ⅳ shape
Ⅱ shape
Ⅰ shape
Standard bucket
Bucket type
Structure Characteristics

## Slide 9: Part 2 Knowledge Related to Shovel Loader Drive Device Structure and Handling Method

## Slide 10: Chapter 1 Structure

## Slide 11: Prime Mover
Figure 2-1 Engine Structure
Figure 2-2 Gasoline Engine Exterior Appearance
Textbook page 31 / Auxiliary Textbook page 11 - 12
Valve Push Rod
Cylinder Head Cover
Fan
Water Pump
V Belt
Timing Gear
Idle Gear
Pump Drive Gear
Oil Pump
Crank Shaft
Connecting Rod
Piston
Cam Shaft
Flywheel
Cylinder Block
Cylinder Head
Exhaust Manifold
Carburetor
Governor
Intake Manifold
Starter
Motor
Oil Pan
(Power Take Off)
Fan Belt
Water Inlet
Fan
Air Intake

## Slide 12: Prime Mover
Figure 2-3 Four-Stroke Engine Process Illustration
Textbook page 31 / Auxiliary Textbook page 12
Connecting Rod
Crankshaft
Intake
Compression
Combustion
Exhaust
Exhaust Valve
Ignition Plug
Intake Valve
Piston Movement Direction

## Slide 13: Prime Mover
Figure 2-4 Diesel Engine Exterior
Textbook page 34 / Auxiliary Textbook page 14
Fuel Filter
Air Intake
Fan Belt
Fan
Water Inlet
Water Outlet
Injection Nozzle
Oil Pan
Fuel Cut Solenoid Valve
Governor
Flywheel Housing
Fuel Injection Pump
Oil Filter

## Slide 14
Figure 2-24 Steering Gear
(Ball nut type)
Textbook page 52 / Auxiliary Textbook page 15
Maneuvering Gear
Gear Case
Worm Shaft
Ball Nut
Sector Shaft

## Slide 15: Maneuvering Gear
Figure 2-25 Semi Integral Type
Figure 2-26 Linkage Type
Textbook page 53/ Auxiliary Textbook page 16 - 17
Oil tool
Needle bearing
Ball nut
Ball
Worm
Gear box
Needle bearing
Plug
Rear guard
Steering shaft
Column
Column bush
Oil tool
Sleeve
Front cover
Spool
O ring
Plug
Ball Sheet
Washer
Spring
Stopper
Washer
Ball sheet
Drag link
Drag link
Booster
Stopper
Spring
Drag link
Plug
Cylinder
To tank
From pump

## Slide 16: Maneuvering Gear
Figure 2-27 Full Hydraulic Pressure Type
Textbook page 54/ Auxiliary Textbook page 18
Handle
Full hydraulic type power steering valve
Hydraulic pressure pump
Rear axle
Rear axle
Steering cylinder
Left
Left

## Slide 17: Maneuvering Gear
Figure 2-28 Drag Link And Tie Rod
Textbook page 55/ Auxiliary Textbook page 19
Bell crank
Tie rod
Drag link

## Slide 18: Braking Device
Figure 2-29 Foot Brake (Example of drum type brake without servo)
Textbook page 56/ Auxiliary Textbook page 20
① Pedal ② Master cylinder ③ Hydraulic pipe④ Wheel cylinder ⑤ Brake shoes ⑥ Brake oil tank
To the parking brake
To the parking brake

## Slide 19: Braking Device
Figure 2-30 Example of Brake Booster (vacuum servo type)
Textbook page 57/ Auxiliary Textbook page 21
Check valve
Vacuum pump
Brake pedal
Master cylinder
Vacuum reserve tank
Brake booster
Wheel cylinder

## Slide 20: Braking Device
Figure 2-31 Internal Expanding Type Brake (double as parking brake too)
Textbook page 58/ Auxiliary Textbook page 22
Cable (left)
When the brake is operated
Parking brake lever
When the brake is released
Cable (right)
Wheel cylinder
(Operated by the foot brake
Brake shoe lining
Brake drum

## Slide 21: Chapter 2 Handling Method

## Slide 22: Instructions Before Starting Work
Table 2-1 Inspection list before starting work
Textbook page 62/ Auxiliary Textbook page 24
Item | Before starting the engine | After starting the engine and in the car | When traveling at a slow speed
Exterior | Water or oil leakage |  | 
Tire | Tire's air pressure, tire damage |  | 
Turn signal and lamp | Stain or damage in the lens and lamp | Every lamp operation | 
Back mirror | Stain, damage | Rear reflection, view | 
Warning device (horn) |  | Is there any sound? | 
Each indicator |  | Each indicator operation | 
Fuel |  | Oil amounts | 
Engine |  | Abnormal sound, exhaust color | 
Clutch |  | Pedal clearance | Clutch disengagement
Foot brake |  | Brake pedal engagement | Brake effective
Parking brake |  | Lever travel, parking brake effectiveness | 
Steering |  | Handle play, looseness | Swing, control
Handling device |  | Handling device operation, bucket ascending and descending movement, dump arm reach operation | 

## Slide 23: Periodic Inspections
Table 2-2 Inspection When Restarting Activities
Textbook page 63/ Auxiliary Textbook page 25
Suspension period | Inspection when restarting activities
Over than 1 month, under one year | Corresponds with monthly inspection
Over than a year | Corresponds with annual inspection

## Slide 24: Guidelines When Starting Operation
Figure 2-33 Starting the gasoline engine type
Figure 2-34 Starting diesel engine type (1)
Figure 2-35 Starting diesel engine type (2)
Textbook page 65/ Auxiliary Textbook page 27
For gasoline engine type, insert the key and turn it to ON position
For diesel engine type (preheat lamp type), turn the key to GLOW position, and turn the preheat signal lamp
For diesel engine type (automatic preheat lamp type), there is also a type where the lamp automatically light up if the key is turned to ON position
Preheat Signal lamp
Preheat Signal lamp

## Slide 25: Guidelines for Starting and Driving
Figure 2-36 Driver seat (clutch type, torque converter type)
Textbook page 67/ Auxiliary Textbook page 29
①Start switch
②Driving injector (displayed when driving)
③Glow injector (diesel engine type vehicle)
④Sedimenter warning light (diesel engine type vehicle)
⑤Battery liquid amount warning light (optional)
⑥Radiator cooling water quantity warning light
⑦Fuel remaining quantity warning light (optional)
⑧Air cleaner element warning light (optional)
⑨Charge warning light
⑩Engine hydraulic pressure warning light
⑪Brake liquid amount warning light
⑫Hour-meter
⑬Engine water temperature gauge
⑭Torque converter type oil temperature gauge (optional)
⑮Fuel meter
⑯Speedometer (optional)
⑰Horn button
⑱Forward-backward lever (torque converter type vehicle)
⑲Forward-backward lever (clutch type vehicle)
⑳High-low speed (speed switcher) lever (clutch type vehicle)
㉑Combination switch (winker and light switch)
㉒Parking brake lever
㉓Fuse box
㉔Accelerator/gas pedal
㉕Brake pedal
㉖Inching pedal (torque converter type vehicle)
Clutch pedal (clutch type vehicle)
㉗Lift lever
㉘Dump lever (without reach function)
㉙Reach lever (with reach function)
㉚Dump lever (with reach function)
㉛Tilt handle lock lever

## Slide 26: Guidelines for Starting and Driving
Figure 2-37 Turning at the Corner
Textbook page 69/ Auxiliary Textbook page 30
Normal truck
Shovel loader

## Slide 27: Guidelines for Stopping, Parking and After Driving
Figure 2-38 Parking Illustration
Textbook page 71/ Auxiliary Textbook page 32

## Slide 28: Operation Precautions
Textbook page 72 / Auxiliary Textbook page 34
(1) Do not drive carelessly.
Pay close attention while driving
and work carefully. A moment of
carelessness can lead to an accident.

## Slide 29: Operation Precautions
Textbook page 72 / Auxiliary Textbook page 34
(2) Do not take eyes off the road when driving. Looking aside while driving can cause a disaster, so pay attention to the direction of travel and pay attention when approaching people working around you.

## Slide 30: Operation Precautions
Textbook page 72 / Auxiliary Textbook page 34
(3) Check the condition of the road
surface and the strength of the
bridge in advance.
Strength, check!

## Slide 31: Operation Precautions
Textbook page 72 / Auxiliary Textbook page 34
(4) Do not drive with people on the
bucket or on the vehicle. It may
cause injury the person when it
suddenly stops.

## Slide 32: Operation Precautions
Textbook page 73 / Auxiliary Textbook page 35
(5) Do not travel with a bucket raised
higher than necessary. (Regardless
of load or no load) lower the bucket
and travel in the basic driving position.

## Slide 33: Operation Precautions
Textbook page 73 / Auxiliary Textbook page 35
(6) On a slippery road, avoid high-speed
driving, high-speed turning, and sudden
braking.

## Slide 34: Operation Precautions
Textbook page 73 / Auxiliary Textbook page 35
(7) On steep slopes, do not drive at right
angle. The vehicle may slip and tip over.

## Slide 35: Operation Precautions
Textbook page 73 / Auxiliary Textbook page 35
(8) Be careful when handling fire. When
bringing fire close to the vehicle, there
is a danger of fire.

## Slide 36: Operation Precautions
Textbook page 74 / Auxiliary Textbook page 36
(9) ① Be sure to face the vehicle when getting on and off the vehicle. Always hold your body in three position or more by using the handrail and the steps.
② Do not jump on or jump off the vehicle
③ Do not get on or get off the vehicle while holding material.
④ Do not get caught in the operating
device accidentally.

## Slide 37: Operation Precautions
Textbook page 74 / Auxiliary Textbook page 36
(10) Be careful of obstacles. When turning
and driving do not collide the vehicle
or the bucket with the obstacles.

## Slide 38: Operation Precautions
Textbook page 74 / Auxiliary Textbook page 36
(11) Obey the running speed at night. At
night, it is easy to get an illusion of
perspective and ground height,
therefore, drive at a speed matches
the lighting.

## Slide 39: Operation Precautions
Textbook page 75/ Auxiliary Textbook page 37
(12) Keep people out of the raised bucket.
Operating the bucket may cause injury.

## Slide 40: Operation Precautions
Textbook page 75/ Auxiliary Textbook page 37
(13) Fully understand the performance of
the vehicle. Bulk materials are easy to
get overload, so be careful not to
overload.

## Slide 41: Operation Precautions
Textbook page 75/ Auxiliary Textbook page 37
(14) Do not load on one side. If you load on
one side, the left and right sides will be
unstable, and the hydraulic system will
be undoable.

## Slide 42: Operation Precautions
Textbook page 75/ Auxiliary Textbook page 37
(15) Be careful when driving on slopes.
When the vehicle is loaded, drive forward on uphill slopes and backward on downhill slopes.
When the vehicle is empty, drive backward on uphill slopes and forward on downhill slopes.
Going
up
Going
down

## Slide 43: Part 3 Knowledge of The Structure and Handling Method of Equipment Related to Cargo Handling Such as Shovel Loaders

## Slide 44: Chapter 1 Structure

## Slide 45: Cargo Handling Equipment
Figure 3-1 Shovel loader work equipment
Textbook page 79 / Auxiliary Textbook page 38
1 Lift arm 2 Connecting road 3 Bucket bracket
4 Bucket 5 Dump cylinder bracket 6 Dump cylinder
7 Lift cylinder

## Slide 46: Cargo Handling Equipment
Figure 3-2 Shovel loader work equipment with reach mechanism
Textbook page 81 / Auxiliary Textbook page 39
1 Lift arm 2 Connecting road 3 Bucket bracket 4 Bucket
5 Dump cylinder bracket 6 Dump cylinder 7 Lift cylinder
8 Reach arm 9 Connecting road B 10 Bell cranck 11 Reach cylinder

## Slide 47: Hydraulic System
Figure 3-3 Excavator loader system diagram
Figure 3-4 Hydraulic pump
Textbook page 82/ Auxiliary Textbook page 40 - 41
Valve controller (Switching)
Hydraulic pump
Valve controller (Switching)
Hydraulic pump
Operation oil filter
Dump cylinder
Lift Cylinder
Lift cylinder
Reach cylinder
Reach
cylinder
Fuel tank operation

## Slide 48: Hydraulic System
Figure 3-5 Control valve
(Double / Standard type)
Figure 3-6 Control valve
(Triple / Standard type)
Textbook page 84 / Auxiliary Textbook page 41 - 42
Safety valve
Dump valve
Reach valve
Lift valve
Bucket backward tilt
Dump lever
Lift lever
Safety valve
Bucket rising
Bucket forward tilt
Bucket descent

## Slide 49: Hydraulic System
Figure 3-7 Opreation of safety valve
Figure 3-8 Control valve operation diagram in neutral
Textbook page 85 / Auxiliary Textbook page 42 - 43
Suspension
Lift cylinder
Safety valve
Dump cylinder
Pump
Hydraulic oil tank
Safety valve
Dump cylinder
Hydraulic pump
Control valve
Dump lever
Lift lever
Suspension

## Slide 50: Hydraulic System
Figure 3- 9 Control valve operation diagram when the lift raise
Figure 3-10 Lift cylinder
Textbook page 86/ Auxiliary Textbook page 43 - 44
Piston
Flow regulator valve
Dust seal
Suspension
U seal
Lift cylinder
Stopper ring
Wear ring
Safety valve
Piston rod guide
Lift cylinder cover
Piston rod
Pull back
Raising

## Slide 51: Hydraulic System
Figure 3-11 Reach and Dump cylinder
Textbook page 87 / Auxiliary Textbook page 44
Piston ring
Dust seal
Holder
Cylinder
U seal
Piston rod
Stopper
U seal
Piston

## Slide 52: Head Guard
Figure 3-12 Head Guard
Textbook page 88/ Auxiliary Textbook page 45
Head Guard

## Slide 53: Fork Loader
Figure 3-13 Pallet Fork
Figure 3-14 Sharp Dumping Fork
Textbook page 89/ Auxiliary Textbook page 46
Pallet forks can perform cargo handling operations the same as forklifts.
The fork, fork bars and backrest are welded together, and the backrest is tilted forward against the fork. It is suitable for the cargo handling work such as lumber, logs, etc.

## Slide 54: Fork Loader
Figure 3-15 Hinged fork
Figure 3-16 Log fork
Textbook page 90 / Auxiliary Textbook page 47
The fork and backrest are designed to be folded by a hydraulic cylinder. If the fork is used at a right angle to the backrest without folding the fork, normal fork work can be performed making it versatile.
The load on fork can be hold on the forks from above with a clamp arm, preventing long objects from falling or wobbling.

## Slide 55: Chapter 2 Handling Method

## Slide 56: Load And Vehicle Stability
Figure 3-25 Load and vehicle stability
Textbook page 98 / Auxiliary Textbook page 49
Lift arm
Lift arm
Maximum reach
Minimum reach
Decrease
Regular

## Slide 57: Load And Vehicle Stability
Figure 3-26 Left-right eccentricity
Figure 3-27 The center of gravity matches the center line
Textbook page 99 / Auxiliary Textbook page 50

## Slide 58: Working Method
Figure 3-28 Uneven surface
Textbook page 100 / Auxiliary Textbook page 52

## Slide 59: Working Method
Figure 3-29 Straight angle
Figure 3-30 Diagonally
Textbook page 101 / Auxiliary Textbook page 53

## Slide 60: Working Method
Figure 3-31 Scooping
Textbook page 102 / Auxiliary Textbook page 54

## Slide 61: Working Method
Figure 3-32 How to turn around corners
Textbook page 103 / Auxiliary Textbook page 55

## Slide 62: Working Method
Figure 3-33 When dumping
Textbook page 104 / Auxiliary Textbook page 56

## Slide 63: Working Method
Figure 3-34 Points when loading
Textbook page 105 / Auxiliary Textbook page 57
Work target
Work target
Work target
Work target

## Slide 64: Working Method
Figure 3-35 Shovel loader with and without reach mechanism
Textbook page 106 / Auxiliary Textbook page 58
Shovel loader without reach mechanism
Shovel loader with reach mechanism

## Slide 65: Part 4 Knowledge of Mechanics Necessary for Driving Shovel Loader Etc.

## Slide 66: Chapter 1 Force

## Slide 67: Moment of Force
Figure 4-9 Moment of force
Figure 4-8 Lever
Textbook page 115 / Auxiliary Textbook page 60

## Slide 68: Moment of Force
Figure 4-10 Moment action on shovel loader
Textbook page 116 / Auxiliary Textbook page 61

## Slide 69: Force Balance
Figure 4-12 Balance with a balance bar
Textbook page 118 / Auxiliary Textbook page 63

## Slide 70: Chapter 2 Mass/Weight and Center of Gravity

## Slide 71: Mass/Weight
Table 4-1 Unit volume mass table of various objects
Textbook page 121 / Auxiliary Textbook page 64
(Note) Wood mass is dry mass, coal and cork are appearance unit weight
Type | Mass per ㎥(t) | Type | Mass per ㎥(t) | Type | Mass per ㎥(t)
Lead | 11.4 | Concrete | 2.3 | Japanese evergreen oak | 0.9
Copper | 8.9 | Brick | 2.2 | Japanese zelkova | 0.7
Steel | 7.8 | Soil | 2.0 | Beech | 0.7
Tin | 7.3 | Pebble | 1.7 | Chestnut | 0.6
Cast iron | 7.2 | Sand | 1.8 | Japanese red pine | 0.5
Zinc | 7.1 | Coal lump | 0.8 | Larch | 0.5
Pig iron | 7.0 | Coal powder | 1.0 | Cedar | 0.4
Aluminum | 2.7 | Cork | 0.5 | Japanese cypress | 0.4
Clay | 2.6 | Water | 1.0 | Paulownia | 0.3

## Slide 72: Mass/Weight
Table 4-2 Volume formula chat
Textbook page 122 / Auxiliary Textbook page 65

## Slide 73: Center of Gravity
Figure 4-15 How to find center of gravity
Textbook page 124 / Auxiliary Textbook page 67

## Slide 74: Stability of Objects
Figure 4-16 Object stability
Textbook page 125 / Auxiliary Textbook page 68

## Slide 75: Chapter 3 Motion of Objects

## Slide 76: Friction
Figure 4－20 Maximum static frictional force and dynamic friction
Textbook page 133 / Auxiliary Textbook page 70
The object is moving
Force applied to the object
Frictional of dynamic
Maximum static
frictional force
Static frictional force
The object is static

## Slide 77: Part 5 Related Laws and Regulations

## Slide 78: Related Laws and Regulations
Figure 5-1 Driving skills legal system for shovel loaders etc.
(Reference) Ministry of Health, Labor and Welfare Risk assessment manual in the building maintenance industry
Textbook page 145 / Auxiliary Textbook page 73
Law
Cabinet
order
Ministerial order
Public announcement Notification
Industrial Safety and Health Act
Order for Enforcement of the Industrial Safety and Health Act
Regulations for Enforcement of the Industrial Safety and Health Act
Structural standards for shovel loader, etc.
Shovel loaders driving skill training rules
Safety and Health Special Education Regulations

## Slide 79: Part 6 Accident Cases

## Slide 80: Case 1 Fall From Shoulder
Case 1 Fall from the shoulder
Textbook page 128 / Auxiliary Textbook page 91

## Slide 81: Case 2 Fall From a Fork Loader Due to Vibration
Case 2 Fall from a fork loader due to vibration
Textbook page 220 / Auxiliary Textbook page 93

## Slide 82: Case 3 While Checking the Condition of a Load, The Worker Was Run Over by a Fork
Case 3 While checking the condition of a load, the worker was run over by a fork
Textbook page 222 / Auxiliary Textbook page 95

## Slide 83: Case 4 Run Over by a Shovel Loader During a Start-up Inspection
Case 4 Run over by a shovel loader during a start-up inspection
Textbook page 224 / Auxiliary Textbook page 97

## Slide 84: Case 5 Shovel Loader Escapes and is Run Over
Case 5 Shovel loader escapes and is run over
Accident situation map
Textbook page 225 / Auxiliary Textbook page 99

## Slide 85: Case 7 Trapped Between Driver’s Seat and Arm During Loading Of Round Steel
Case 7 Trapped between driver’s seat and arm during loading of round steel
Textbook page 229 / Auxiliary Textbook page 101

## Slide 86: Case 8 Trapped Between the Machine And The Built-in Sheet Pile
Case 8 Trapped between the machine and the built-in sheet pile
Textbook page 231 / Auxiliary Textbook page 103

## Slide 87: Case 9 Head Caught in the Arm of the Shovel Loader
Case 9 Head caught in the arm of the shovel loader
Accident situation map (side view)
Accident situation map (plan view)
Textbook page 233 / Auxiliary Textbook page 106
Iron
piece
Lift arm up and down
Operation lever
Victim
Driving seat
Shovel
Shovel
Lift arm
Driver's seat leg
Part cover plate
Victim(A)
Shovel operation lever
Lift arm
Driver's seat leg cover plate

## Slide 88
Case 10 A concrete block lifted by the shovel loader falls and was damaged
Situation diagram of lifting a block with a bucket
Textbook page 233 / Auxiliary Textbook page 108
Case 10 A Concrete Block Lifted by The Shovel Loader Falls and Was Damaged
Bucket
Concrete block